## Slide 1: Life Cycle Analysis in Electronics
2025

## Slide 2: Agenda
Course 2 – Life Cycle Analysis in electronics
LCA Process and environmental challenges

## Slide 3: Life cycle
Natural resources
Material production
Use
Product manufacture
Company
A
Company
B
Gate to gate
Cradle to gate
End-of-life
management
Reuse
Recycle
Cradle to grave
Combust
Landfill
Ecological loop
Cradle to cradle
Inputs/outputs
Inputs/outputs
Inputs/outputs
Inputs/outputs
Inputs/outputs

## Slide 4: Life cycle
Natural resources
Material production
Use
Product manufacture
Company
A
Company
B
Gate to gate
Cradle to gate
End-of-life
management
Reuse
Recycle
Cradle to grave
Combust
Landfill
Ecological loop
Cradle to cradle
Inputs/outputs
Inputs/outputs
Inputs/outputs
Inputs/outputs
Inputs/outputs


## Slide 5: Life cycle
Natural resources
Material production
Use
Product manufacture
Company
A
Company
B
Gate to gate
Cradle to gate
End-of-life
management
Cradle to grave
Combust
Landfill
Inputs/outputs
Inputs/outputs
Inputs/outputs
Inputs/outputs
Inputs/outputs

## Slide 6: Electronics end-of-life
UN Global waste monitor
  In 2022 62 million tons of e-waste, including 2.5Mt from France (4 %)
Ecosystem (Responsabilité élargie du producteur (REP), in 2023
  Type (Collection rate (taux de collecte), recycling rate)
  Household WEEE 640 ktons (47%, 78%)
  Professional WEEE 89 ktons (42% 84%)
  Lamps 5,5 ktons (89%, 85%)
Ecologic, in 2023, 120 partners for recycling
  Household WEEE 215 ktons (57%, 77%)
  Professional WEEE 83 ktons (67%, 78%)
Video of a DEEE recycling process
Notes: Le taux de collecte établit le rapport entre la quantité de déchets collectés auprès de producteurs identifiés et la quantité totale des déchets produits par ces mêmes producteurs.
Pour un matériau ou un type de produits donné, le taux de recyclage correspond à la quantité de déchets recyclés dans le courant d'une année civile par rapport au total des déchets produits.
=(640/0,47)+(89/0,42)+(5,5/0,89)+(215/0,57)+(83/0,67)
Exemple d’information Ecosystem
La collecte, le traitement et la dépollution des DEEE ne s'improvisent pas ! Supervisées et contrôlées par Ecologic pour le compte de ses producteurs adhérents, ces étapes sont assurées à ce jour par 120 opérateurs partenaires, qui doiventrépondre à des critères de qualité et de suivi très précis. Paprec est l'un d'entre eux. Sur ces 40 usines installées en France, cinq sont chargées de la collecte, du démantèlement et de la dépollution de plus de 10 000 tonnes de DEEE par an. « Depuis trois ans, explique Miguel Lauga, directeur délégué de Paprec, nous ne cessons de moderniser nos équipements pour répondre aux normes de traitement et améliorer le taux de dépollution des composants issus des DEEE. Et bien que notre activité principale porte sur le démantèlement des écrans, le groupe PAPREC s'intéresse aussi à d'autres produits tels le PAM (Petits Appareils en Mélange). » Bien que leur taux de valorisation soit inférieur aux PAM, les écrans nécessitent des chaînes de traitements spécifiques, notamment pour extraire les poudres luminescentes. « Notre site situé à Bordeaux, ajoute Miguel Lauga, vient d'être équipé d'un système confiné d'aspiration centrale qui permet aux équipes de travailler dans de meilleures conditions : un tapis de convoyage et un basculeur automatique acheminent les écrans sans que les opérateurs aient à se déplacer d'un poste de travail à un autre ; l'émission et la perte de poussières sont limitées ; la séparation des verres au plomb et des verres au baryum est optimisée au profit d'un meilleur taux de dépollution, etc. Ce type d'équipement nous permet de répondre aux exigences des audits conduits par Ecologic. Il nous offre aujourd'hui la possibilité de nous inscrire comme un acteur clé du traitement des écrans ».

## Slide 7: 2- Life Cycle Inventory
Life cycle assessment framework
Direct applications:
Product development and improvement
Strategic planning
Public policy making
Marketing
Other
ISO 14040
Goal and scope definition
1
Inventory analysis
2
Impact assessment
3
Interpretation
4

## Slide 8: Life cycle
Natural resources
Material production
Use
Product manufacture
Company
A
Company
B
Gate to gate
Cradle to gate
End-of-life
management
Reuse
Recycle
Cradle to grave
Combust
Landfill
Ecological loop
Cradle to cradle
Inputs/outputs
Inputs/outputs
Inputs/outputs
Inputs/outputs
Inputs/outputs

## Slide 9: Ecosphere/Technosphere Foreground/Background
Example of a PCB producer and integrator
From ESOS, inspired from
JRC-IEA (2010) International Reference Life Cycle Data System (ILCD) Handbook—General guide for Life Cycle Assessment—Detailed guidance. First edition March 2010. Publications Office of the European Union, Luxembourg. Available at http://lct.jrc.ec.europa.eu/
Notes: Foreground/background distinction
Specificity perspective: where specific data should be used versus where average or generic background data can typically be used by default
management perspective: identifying which processes can be underdirect control or decisive influence from the point of view of the decision-context of a study
Foreground: own operations and fixed suppliers - data for the specific e.g. technology, supplier etc. is most appropriate.
Background: purchased via a (theoretically fully homogenous) market - averaging effect across the suppliers

## Slide 10: Ecosphere/Technosphere Foreground/Background
Example of a PCB producer and integrator
From ESOS, inspired from
JRC-IEA (2010) International Reference Life Cycle Data System (ILCD) Handbook—General guide for Life Cycle Assessment—Detailed guidance. First edition March 2010. Publications Office of the European Union, Luxembourg. Available at http://lct.jrc.ec.europa.eu/
Notes: Foreground/background distinction
Specificity perspective: where specific data should be used versus where average or generic background data can typically be used by default
management perspective: identifying which processes can be underdirect control or decisive influence from the point of view of the decision-context of a study
Foreground: own operations and fixed suppliers - data for the specific e.g. technology, supplier etc. is most appropriate.
Background: purchased via a (theoretically fully homogenous) market - averaging effect across the suppliers

## Slide 11: Inventory data retrieval
Foreground/background distinction
  Foreground: own operations and fixed suppliers
    data for the specific e.g. technology, supplier etc. is most appropriate.
    Primary data
  Background: purchased via a (theoretically fully homogenous) market
    Averaging effect across suppliers makes databases relevant
    Secondary data
  Two perspectives
    Specificity perspective: foreground = where specific data should be used versus background = where average or generic data can be used by default
    management perspective: foreground = processes under direct control or decisive influence from the point of view of the decision-context of a study

## Slide 12: 2 - Life Cycle Inventory
Inputs / outputs list
  Raw materials, chemicals
  Energy, water, air
  Packaging
  Transport
  Waste
  …
https://shop.fairphone.com/fr/fairphone-4

## Slide 13: Mathematical methods for cost computation
The linear assumption dominates
  Producing N times more costs N times more
Several mathematical methods
  Linear sequential cost aggregation
  Linear matrix cost aggregation
  Non-linear cost aggregation

## Slide 14: Cost computation
Phone case
1
Phone camera
1
Phone electronics
1
Phone assembly
1
CO2
1
kg
Electricity
1
kWh
Phone display
1
Phone battery
4
Ah
Smartphone
1
Reference flow
  Amount of product or service to reach functional unit.
Notes: A droite, le LCI. On étudie la génération d’électricité.

## Slide 15: Sequential computation : an example
(
1
kWh
Electricity generation
Electricity
1
kWh
CO2
1
kg
1
L
Oil
Notes: Génération d’1 kWh d’électricité.

## Slide 16: Sequential computation: an example
CO2
1
kg
1
L
Oil extraction
Electricity
0.2
kWh
1
L
Oil
Notes: Produire 1l de pétrole consomme de l’électricité => récursif

## Slide 17: Sequential computation : an example
kWh
L
L
kWh
Notes: Question : combien de chaque process (production d’électricité et production de prétrole) faut-il pour produite un flux de référence (par exemple 1kWh d’électricité)?

## Slide 18: Sequential computation
kWh
kWh
kWh
Notes: Suite récursive. Ligne 2, on remplace 0,2kWh par l’équivalent de la ligne 1.

## Slide 19: Sequential computation
kWh
kWh
kWh
Notes: Suite récursive 1+0,2+0,2^2+0,2^3+… pour produire 1kWh, suite qui tend vers 1,25,

## Slide 20: Matrix computation
Heijungs, R., & Suh, S. (2002). The computational structure of life cycle assessment (Vol. 11). Springer Science & Business Media.
Technosphere
Processes
Flows
+  produce
-  consume
Notes: On pose le même problème au format matrice.
A = technosphère (échanges entre process et produits)
Se lit en colonne:
Pour produire 1kWh d’électricité, on consomme 1l de pétrole.
Produire 1l de pétrole consomme 0,2kWh d’électricité.

## Slide 21: Matrix computation
Reference flow (1kWh)
Scaling factor
Notes: f = reference flow, produire 1kWh d’électricité.
On cherche à résoudre S.
S: scaling factor : quantité de chaque process pour produire le reference flow

## Slide 22: Matrix computation
Notes: S: scaling factor : quantité de chaque process pour produire le reference flow

## Slide 23: Matrix computation
Notes: S: scaling factor : quantité de chaque process pour produire le reference flow

## Slide 24: Matrix computation
Ecosphere = Biosphere
Cost
Notes: B = biosphère (ce qui est ajouté et extrait de l’environnement) 1kWh d’électricité et 1l de pétrole.
ce que coûte chaque process
g = quantité d’externalités (ecosphere)
Hypothèse ici: 1 kg CO2 emis par kWh d’électricité et par L de pétrole

## Slide 25: Matrix computation
kg CO2

## Slide 26: Model definition
R and
Cost
Cost per process
Amount of each process to produce functional unit
Link process-flow (in columns)
Reference flow
Notes: Functional unit (reference flow)

## Slide 27: Model definition
R and

## Slide 28: Model definition
R and
Notes: Using Ecoinvent/Brightway, we build f and complete A

## Slide 29: Life-Cycle Inventory = produce f
Heijungs, R., & Suh, S. (2002). The computational structure of life cycle assessment (Vol. 11).
Springer Science & Business Media.
Notes: Using Ecoinvent/Brightway, we build f (and complete A)

## Slide 30: 2 - Life Cycle Inventory
Data quality
Reliability
Exhaustiveness
Temporal correlation
Geographical correlation
Technological correlation

## Slide 31: 2 - Life Cycle Inventory
Primary data
  Real world data
  Manufacturer data
  Teardown
  Materials identification
  Size, weight measurements
  …
Baur, S-J.; Proske, M.; Poppe, E. LCA of the Framework Laptop 2022. Fraunhofer IZM, 2023,
https://downloads.frame.work/resources/Framework-Life-Cycle-Report.pdf

## Slide 32: 2 - Life Cycle Inventory
Secondary data
  Estimation, equivalent data
  Competitor datasheet
  Company reports
  Expert judgment
  …
Baur, S-J.; Proske, M.; Poppe, E. LCA of the Framework Laptop 2022. Fraunhofer IZM, 2023,
https://downloads.frame.work/resources/Framework-Life-Cycle-Report.pdf

## Slide 33: 2 - Life Cycle Inventory
Impact databases
  Ecoinvent
  Negaoctet
  Sphera LCA Database (GaBi)
  Bureau Veritas CODDE/EIME
  …
Tools
  Brightway
  OpenLCA
  Ecodesign Studio
  Bureau Veritas CODDE
  …
Baur, S-J.; Proske, M.; Poppe, E. LCA of the Framework Laptop 2022. Fraunhofer IZM, 2023,
https://downloads.frame.work/resources/Framework-Life-Cycle-Report.pdf

## Slide 34: Data bases = Matrix A
Notes: Using Ecoinvent/Brightway, we build f and complete A

## Slide 35: 2 - Life Cycle Inventory
Example
Phone battery

## Slide 36: 2 - Life Cycle Inventory
Example
Lifetime
Phone battery
1000 cycles
Recharge
14.8 Wh/cycle
Capacity
3905 mAh / 15.03 Wh
Weight
64.2g
Technology
Lithium ion
Localisation
China
14.38 Wh
13.42 Wh
10.21 Wh
Battery cell production, Li-ion, NCA
Date 2017
Capacity 224 Wh/kg
Localisation China
Battery cell production, Li-ion, NMC811
Date 2017
Capacity 209 Wh/kg
Localisation China
Battery cell production, Li-ion, LFP
Date 2016
Capacity 159 Wh/kg
Localisation China
Unit kg
Unit kg
Unit kg
Notes: NMC, NCA, LFP: sous-catégories de batteries lithium ion
Question avant de répondre: laquelle choisir?

## Slide 37: 2 - Life Cycle Inventory
Example
Phone display

## Slide 38: 2 - Life Cycle Inventory
Example
Phone display
Technology
LCD
Surface
97.4 cm2
Resolution
1080 x 2340 pixels
Pixels density
410 ppp
Localisation
China
Liquid crystal display production, unmounted
Date 2007
Unit kg
Localisation Global

## Slide 39: 2 - Life Cycle Inventory
Example
Phone display
Technology
LCD
Surface
97.4 cm2
Resolution
1080 x 2340 pixels
Pixels density
410 ppp
Localisation
China

## Slide 40: 2 - Life Cycle Inventory
Example
Localisation
Taiwan
Date
2022
Production
60 475 995 m²
Scope 1
69.7 kt CO2e
Scope 2
2 373.4 kt CO2e
Scope 3
1 004.5 kt CO2e
Phone display
Technology
LCD
Surface
97.4 cm2
Resolution
1080 x 2340 pixels
Pixels density
410 ppp
Localisation
China

## Slide 41: Agenda
Impact assessment
Assigning numbers

## Slide 42: 3- Impact assessment
Life cycle assessment framework
Direct applications:
Product development and improvement
Strategic planning
Public policy making
Marketing
Other
ISO 14040
Goal and scope definition
1
Inventory analysis
2
Impact assessment
3
Interpretation
4

## Slide 43: Impact assessment = produce g
Notes: Using Ecoinvent/Brightway, we build f and complete A

## Slide 44: Challenges of impact assessment
Environmental impacts of human activities are complex
  Global warming
  Destruction of forest
  Pollution of land, water and air
  Consumption of non-renewable resources
Impact assessment methods standardize evaluations
  Impact categories
  Units and aggregation methods
  Mid-point and end-point impacts

## Slide 45: EU resources on impact assessment
EPLCA : European Platform on LCA (European Commission)
  DG ENV : responsible for the EU Commission's policies on the environment
  JRC (Joint Research Centre) : Scientific support to EF development
  ILCD 2010 (International Life Cycle Data system)
    Technical guidance
    LCI & LCIA phases
Notes: EF: Environmental Footprint
PEF: Product Environmental Footprint

## Slide 46: EU resources on impact assessment
EPLCA : European Platform on LCA (European Commission)
  DG ENV : responsible for the EU Commission's policies on the environment
  JRC (Joint Research Centre) : Scientific support to environmental footprint development
  EF (Environmental Footprint) 2013 : LCA methods
    Recommendation 2021/2279 of the EU Commission
    PEF : products
      Provides impacts for elementary flows
    OEF : organisations
    Data & tools development
  Standardizing environmental impacts and their assessment

## Slide 47: EU EF provides matrix B
Notes: Using Ecoinvent/Brightway, we build f and complete A

## Slide 48: EU resources on impact assessment
EPLCA : European Platform on LCA (European Commission)
  DG ENV : responsible for the EU Commission's policies on the environment
  JRC (Joint Research Centre) : Scientific support to environmental footprint development
  LCDN (Life Cycle Data Network)
    Nodes network
    Publish LCA data
    Search shared data
    Harmonized practices, quality

## Slide 49: 16 mid-point impacts, 5 very critical for electronics
Climate change
Ozone depletion
Photochemical ozone formation, human health
Water use
Particulate matter
Resource use, fossils
Resource use, minerals and metals
Acidification
Ionising radiation, human health
Eutrophication, marine
Eutrophication, freshwater
Human toxicity, non-cancer
Eutrophication, terrestrial
Land use
Ecotoxicity, freshwater
Human toxicity, cancer
Notes: Ocean acidification -> jeopardizes animals and plants
Eutrophication -> (azote et de phosphore) nitrogen and phosphorus -> develop algae -> deplete oxygen

## Slide 50: Mid-point to end-point impacts (example)
Ismaeel, W. S. (2018). Midpoint and endpoint impact categories in
Green building rating systems. Journal of Cleaner Production, 182, 783-793

## Slide 51: 16 impacts, 5 very critical for electronics
Climate change
Ozone depletion
Photochemical ozone formation, human health
Water use
Particulate matter
Resource use, fossils
Resource use, minerals and metals
Acidification
Ionising radiation, human health
Eutrophication, marine
Eutrophication, freshwater
Human toxicity, non-cancer
Eutrophication, terrestrial
Land use
Ecotoxicity, freshwater
Human toxicity, cancer
Notes: Ocean acidification -> jeopardizes animals and plants
Eutrophication -> (azote et de phosphore) nitrogen and phosphorus -> develop algae -> deplete oxygen

## Slide 52: 16 impacts, 5 very critical for electronics
Climate change
Ozone depletion
Photochemical ozone formation, human health
Water use
Particulate matter
Resource use, fossils
Resource use, minerals and metals
Acidification
Ionising radiation, human health
Eutrophication, marine
Eutrophication, freshwater
Human toxicity, non-cancer
Eutrophication, terrestrial
Land use
Ecotoxicity, freshwater
Human toxicity, cancer
Unit : kg CO2e
Climate change
Localisation : Global
Consequences include extreme weather events, rising sea levels, melting glaciers, ecosystem degradation, threats to food security and increased risks to human health.
Notes: Ocean acidification -> jeopardizes animals and plants
Eutrophication -> (azote et de phosphore) nitrogen and phosphorus -> develop algae -> deplete oxygen
Land use index aggregates five midpoint indicators to assess the impact of land use on soil quality: 1) erosion resistance, 2) physicochemical filtration, 3) groundwater regeneration, 4) mechanical filtration and 5) biotic production.

## Slide 53: Focus on global warming and greenhouse gases emissions
“The lifetime of fossil fuel CO2 in the atmosphere is a few centuries, plus 25 percent that lasts essentially forever. The next time you fill your tank, reflect upon this”, D. Archer.
EF model = GWP100 (Global Warming Potentials over 100 years)
Semiconductor fabrication gas examples
  1kg Sulfur Hexafluoride (SF6) = 23,900 kg CO2e, remains 3,200 years in atmosphere
  1kg Trifluoromethane (HFC-23) (CHF3) = 11,700 kg CO2e , remains 264 years in atmosphere
  1kg Perfluoromethane (CF4) = 6,500 kg CO2e , remains 50,000 years in atmosphere
Bartos, S. C., & Burton, C. S. (2002). PFC, HFC, NF3, and SF6 emissions from semiconductor manufacturing. Good Practice Guidance and Uncertainty Management in National Greenhouse Gas Inventories, 1-13.
Archer, D. The Long Thaw: How Humans Are Changing the Next 100,000 Years of Earth's Climate (Princeton Univ. Press, 2008).

## Slide 54: GHG Emissions objective
Human GHG emissions reach 60Gt/year
To respect the 1.5°C scenario of the Paris Agreement, emissions must reach 8Gt/year by 2050, i.e. a reduction of ~7× by 2050
8Gt
The Closing Window: Climate crisis calls for rapid transformation of societies,
UN environment program 2022

## Slide 55: GHG Emissions objective
Human GHG emissions reach 60Gt/year
To respect the 1.5°C scenario of the Paris Agreement, emissions must reach 8Gt/year by 2050, i.e. a reduction of ~7× by 2050
8Gt
Chart: 
| 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Série 1 | 59 | 55.165 | 51.5793 | 48.2266 | 45.0919 | 42.1609 | 39.4205 | 36.8581 | 34.4624 | 32.2223 | 30.1278 | 28.1695 | 26.3385 | 24.6265 | 23.0258 | 21.5291 | 20.1297 | 18.8213 | 17.5979 | 16.454 | 15.3845 | 14.3845 | 13.4495 | 12.5753 | 11.7579 | 10.9937 | 10.2791 | 9.6109 | 8.9862 | 8.4021 | 7.856 | 7.3453
-7%/year

## Slide 56: GHG Emissions objective
The manufacture of integrated circuits emitted 76Mt CO2eq in 2021, an increase of 13% compared to 2020.
For +28% revenue: efficiency has improved, sustainability has not.
The current study excludes Scope 3.
Maxime Pelcat. GHG emissions of semiconductor manufacturing in 2021. Research Report. 2023. ⟨hal-04112708⟩

## Slide 57: 16 impacts, 5 very critical for electronics
Climate change
Ozone depletion
Photochemical ozone formation, human health
Water use
Particulate matter
Resource use, fossils
Resource use, minerals and metals
Acidification
Ionising radiation, human health
Eutrophication, marine
Eutrophication, freshwater
Human toxicity, non-cancer
Eutrophication, terrestrial
Land use
Ecotoxicity, freshwater
Human toxicity, cancer
Unit : m3 water equivalent
Water use
Localisation : Local
Consequences are lack of water for humans, plants or animals, and withdrawal of water from rivers, lakes and groundwater.
Notes: Ocean acidification -> jeopardizes animals and plants
Eutrophication -> (azote et de phosphore) nitrogen and phosphorus -> develop algae -> deplete oxygen

## Slide 58: 16 impacts, 5 very critical for electronics
Climate change
Ozone depletion
Photochemical ozone formation, human health
Water use
Particulate matter
Resource use, fossils
Resource use, minerals and metals
Acidification
Ionising radiation, human health
Eutrophication, marine
Eutrophication, freshwater
Human toxicity, non-cancer
Eutrophication, terrestrial
Land use
Ecotoxicity, freshwater
Human toxicity, cancer
Unit : MJ
Ressource use, fossils
Localisation : Local
Consequences are depletion of oil, gas and coal, no more usable for other means.
Notes: Ocean acidification -> jeopardizes animals and plants
Eutrophication -> (azote et de phosphore) nitrogen and phosphorus -> develop algae -> deplete oxygen

## Slide 59: 16 impacts, 5 very critical for electronics
Climate change
Ozone depletion
Photochemical ozone formation, human health
Water use
Particulate matter
Resource use, fossils
Resource use, minerals and metals
Acidification
Ionising radiation, human health
Eutrophication, marine
Eutrophication, freshwater
Human toxicity, non-cancer
Eutrophication, terrestrial
Land use
Ecotoxicity, freshwater
Human toxicity, cancer
Unit : Point
Land use
Localisation : Local
Land use index aggregates five midpoint indicators to assess the impact of land use on soil quality:
1) erosion resistance,
2) physicochemical filtration,
3) groundwater regeneration,
4) mechanical filtration and
5) biotic production.
Notes: Ocean acidification -> jeopardizes animals and plants
Eutrophication -> (azote et de phosphore) nitrogen and phosphorus -> develop algae -> deplete oxygen

## Slide 60: 16 impacts, 5 very critical for electronics
Climate change
Ozone depletion
Photochemical ozone formation, human health
Water use
Particulate matter
Resource use, fossils
Resource use, minerals and metals
Acidification
Ionising radiation, human health
Eutrophication, marine
Eutrophication, freshwater
Human toxicity, non-cancer
Eutrophication, terrestrial
Land use
Ecotoxicity, freshwater
Human toxicity, cancer
Unit : kg Sb equivalent
Ressource use, minerals and metals
Localisation : Local
Consequences are depletion of metals and materials extracted from earth.
Notes: Ocean acidification -> jeopardizes animals and plants
Eutrophication -> (azote et de phosphore) nitrogen and phosphorus -> develop algae -> deplete oxygen
Sb: antimoine

## Slide 61: 16 impacts, 5 very critical for electronics
Climate change
Ozone depletion
Photochemical ozone formation, human health
Water use
Particulate matter
Resource use, fossils
Resource use, minerals and metals
Acidification
Ionising radiation, human health
Eutrophication, marine
Eutrophication, freshwater
Human toxicity, non-cancer
Eutrophication, terrestrial
Land use
Ecotoxicity, freshwater
Human toxicity, cancer
Notes: Ocean acidification -> jeopardizes animals and plants
Eutrophication -> (azote et de phosphore) nitrogen and phosphorus -> develop algae -> deplete oxygen

## Slide 62: Impact categories
https://eplca.jrc.ec.europa.eu/uploads/JRC128571_S4P_ConsumptionFootprint.pdf
CC BY European Union 2023
6.8Gt CO2e/y
Notes: Global normalisation factors = diviser le résultat de l’impact permet de les comparer entre eux avec une unité commune.
Weighting factors = importance de l’impact par rapport aux autres. Impact à traiter en priorité (considération subjective, selon les pays).
GWP planetary boundary 6,81 Gt CO2e (valeur absolue annuelle)

## Slide 63: Impact categories
https://eplca.jrc.ec.europa.eu/uploads/JRC128571_S4P_ConsumptionFootprint.pdf
CC BY European Union 2023

## Slide 64: Impact categories
https://eplca.jrc.ec.europa.eu/uploads/JRC128571_S4P_ConsumptionFootprint.pdf

## Slide 65: Impact categories
https://eplca.jrc.ec.europa.eu/uploads/JRC128571_S4P_ConsumptionFootprint.pdf

## Slide 66: Interpretation
Life cycle assessment framework
Direct applications:
Product development and improvement
Strategic planning
Public policy making
Marketing
Other
ISO 14040
Goal and scope definition
1
Inventory analysis
2
Impact assessment
3
Interpretation
4

## Slide 67: Interpretation : attributional LCA

## Slide 68: Interpretation : consequential LCA
Smartphone
1
Phone
1
Water use
Raw materials
Climate change
impacts
impacts
Water use
Raw materials
Climate change

## Slide 69: Nine planetary boundaries
Richardson, K., Steffen, W., Lucht, W., Bendtsen, J., Cornell, S.E., Donges, J.F., Drüke, M., Fetzer, I., Bala, G., von Bloh, W., Feulner, G., Fiedler, S., Gerten, D., Gleeson, T., Hofmann, M., Huiskamp, W., Kummu, M., Mohan, C., Nogués-Bravo, D., Petri, S., Porkka, M., Rahmstorf, S., Schaphoff, S., Thonicke, K., Tobian, A., Virkki, V., Weber, L. & Rockström, J. 2023. Earth beyond six of nine planetary boundaries. Science Advances 9, 37. 10.1126/sciadv.adh2458
Climate change (CO2) concentration
  2015 Paris Agreement 1,5°C
Safe
Increasing risk
High risk
280 ppm
CO2 concentration (ppm)
Preindustrial
350 ppm (~1°C)
450 ppm (~2°C)
Current 417 ppm
Notes: Faire deviner les valeurs ppm aux étudiants.
Cycle azote et phosphore -> engrais
L’eau « bleue » est celle qui transite rapidement dans les cours d’eau, les lacs, les nappes phréatiques… vers la mer. Elle représente environ 40% de la masse totale des précipitations, souvent appelées « précipitations efficaces ». Par opposition à des précipitations non-efficaces ? Cette sémantique démontre de l’intérêt pour ce qu’on voit directement, au détriment de ce qui se révèle pourtant le plus important : les 60% du reste des précipitations, qui alimentent « l’eau verte ».
L’eau « verte » est cette eau qui est stockée dans le sol et la biomasse. Elle peut être évaporée par les sols, ou absorbée puis évapotranspirée par les plantes. En termes de flux d’eau douce, c’est l’eau la plus importante. On sait de fait que les plantes gèrent elles-mêmes le cycle de l’eau.

## Slide 70: Global warming forecast
IPCC, 2023: Summary for Policymakers. In: Climate Change 2023: Synthesis Report. Contribution of Working Groups I, II and III to
the Sixth Assessment Report of the Intergovernmental Panel on Climate Change [Core Writing Team, H. Lee and J. Romero (eds.)].
IPCC, Geneva, Switzerland, pp. 1-34, doi: 10.59327/IPCC/AR6-9789291691647.001
IPCC (en) = GIEC (fr)

## Slide 71: Agenda
LCA limits

## Slide 72: LCA limits
Electric car
Gasoline car
Hydrogen car
H
Notes: Suite à une LCA, on pourrait dire que l’hydrogène est une solution technique.

## Slide 73: LCA limits
Electric car
Gasoline car
Hydrogen car
H
Kerosene plane
Hydrogen plane
H
Notes: Seulement on ne peut pas l’appliquer à l’ensemble du parc, notamment en aviation.
LCA = mesure, pas une solution.

## Slide 74: Rebound effect
Electric car
Use
Production
impacts
Use
Production
impacts
Gasoline car
Notes: Paradoxe de Jevons, livre de 1865, sur la question du charbon.

## Slide 75: Thanks