## Slide 1: Life Cycle Analysis in Electronics
2025

## Slide 2: Agenda
Course 3 – Life Cycle Analysis in electronics
Regulations and Challenges

## Slide 3: Sustainability
A society may in many ways compromise its ability to meet the essential needs of its people in the future - by overexploiting resources, for example. The direction of technological developments may solve some immediate problems but lead to even greater ones.
Brundtland, G. H. (1987). Our common future—Call for action. Environmental conservation, 14(4), 291-294.

## Slide 4: What is sustainable electronics?
Sustainable electronics is electronics that
  meets the needs of present generations without compromising the ability of future generations to meet their own needs.
  Brundtland report – “Our Common Future”, the United Nations, 1987
3 pilars
  Environmental
  Social
  Economic
Maslow’s pyramid
Notes: What are the needs of current generation?
How do we compromise the needs of future generations?

## Slide 5: Human carbon impact
8Gt
Chart: 
| 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Série 1 | 59 | 55.165 | 51.5793 | 48.2266 | 45.0919 | 42.1609 | 39.4205 | 36.8581 | 34.4624 | 32.2223 | 30.1278 | 28.1695 | 26.3385 | 24.6265 | 23.0258 | 21.5291 | 20.1297 | 18.8213 | 17.5979 | 16.454 | 15.3845 | 14.3845 | 13.4495 | 12.5753 | 11.7579 | 10.9937 | 10.2791 | 9.6109 | 8.9862 | 8.4021 | 7.856 | 7.3453
-7%/year
Human GHG emissions reach 60Gt/year
To respect the 1.5°C scenario of the Paris Agreement, emissions must reach 8Gt/year by 2050, i.e. a reduction of ~7× by 2050

## Slide 6: Human carbon impact per sector (in France)
Chart: 
| Transportation | Agriculture | Construction | Industry | Energy | Waste
Territorial emissions in France in 2018 (Mt CO2e) | 137 | 86 | 84 | 79 | 46 | 14
Suivi de la Stratégie Nationale Bas-Carbone
Indicateurs de résultats
Ministère de la Transition Ecologique, 2021

## Slide 7: Two strategies to distribute efforts
Chart: 
| Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible
Territorial emissions | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01
Chart: 
| Transportation | Agriculture | Construction | Industry | Energy | Waste
Territorial emissions in France in 2018 (Mt CO2e) | 137 | 86 | 84 | 79 | 46 | 14
Chart: 
| Transportation | Agriculture | Construction | Industry | Energy | Waste
Territorial emissions in France in 2018 (Mt CO2e) | 137 | 86 | 84 | 79 | 46 | 14
1
2

## Slide 8: Cloud
Services
Mobility
E-commerce
Data storage
and backup
Data
manipulation
Education
Management
Social
Media
Entertainment
Credits:
Iconjam, freepik, srip, monkik,
The Chohans Brand, vectorspoint, mynamepong
IconBandaar, Futuer, vectorsmarket15, Muhammad Atif,
Dendrogram
Edge devices /
data sources
Core cloud /
network
Fog resources /
edge network

## Slide 9: Cloud
Services
Mobility
E-commerce
Data storage
and backup
Data
manipulation
Education
Management
Social
Media
Entertainment
Credits:
Iconjam, freepik, srip, monkik,
The Chohans Brand, vectorspoint, mynamepong
IconBandaar, Futuer, vectorsmarket15, Muhammad Atif,
Dendrogram
Edge devices /
data sources
Core cloud /
network
Fog resources /
edge network

## Slide 10: Human carbon impact (in France)
CO2e is a global metric for global warming impact
  other greenhouse gases (GHG) are converted in equivalent CO2
  One can distinguish (French numbers)
    inventaire national (domestic footprint): ~6.4t/person (in 2018) : quantities of greenhouse gases (GHG) produced on the French territory
    Carbon footprint (consumption footprint): 11.2t/ person (in 2018) : domestic consumption of goods and services, both domestically produced and imported

## Slide 11: Carbon accounting
Greenhouse Gas Protocol and ISO 14064 (Organisation emissions)
  Employing an accounting method for carbon emission tracking (in tons of CO2 equivalent) to avoid double counting
  Scope 1: GHG direct emissions from activity
  Scope 2: GHG emissions from energy consumption
    Location-based: reflects the average emissions intensity of grids on which energy consumption occurs
    Market-based: taking into account, derives emission factors from contractual instruments (e.g. REC)
      renewable energy certificates (RECs)
  Scope 3: Indirect emissions from value chain (up and downstream)

## Slide 12: Semiconductors and GHG emissions
Scope 3 upstream emissions
  Mining materials
  Smelting
  Refining
    High temperature processes for wafer production: reducing silicon from SiO2, purifying silicon, building single crystal silicon ingots
Scope 3 downstream emissions
  Transporting products
  Using products
  End-of-life
Impacts of electronics are increasingly well understood
Greenhouse Gas Protocol, World Resources Institute, Revised edition, 2015
Client
Notes: Ultrapure water, ultrapure silicium, coper, aluminum…

## Slide 13: Supply chain (in general)
Industry employs a supply chain pyramid with Tiers
…
OEM: Original Equipment Manufacturer
TIER 1: Module or system supplier
TIER 2: Component supplier
TIER 3: Sub-component supplier
TIER N: Natural resource supplier
Flaticons: Mehwish, Freepik

## Slide 14: The electronics industry supply chain
Industry employs a supply chain pyramid with Tiers
…
OEM: Original Equipment Manufacturer
TIER 1: PCBA supplier
TIER 2: Integrated circuit supplier
TIER 3: wafer supplier
TIER N: Minerals supplier
Flaticons: Surang, Kerismaker, Freepik, smashicons

## Slide 15: Electronic devices
Sensors
Power Management
Actuators
Computing
Communication / Networking
Storage
Hardware Interface
Operating System
Libraries
Applications
Drivers
Electronic equipment
Electrical equipment
From another energy to electrical energy
From electrical energy to another energy

## Slide 16: Electronics market and Europe (in 2017)
Now 600+ B€
Notes: Semiconductor: 600B today, 1T in 2030

## Slide 17: The case of global warming
All human activities produce CO2
Mt CO2 / year in France
Total: 749 Mt CO2
in 2018

## Slide 18: The case of global warming
All human activities produce CO2
Mt CO2 / year in France
Total: 749 Mt CO2
in 2018
Electronics is here

## Slide 19: The case of global warming
All human activities produce CO2
Mt CO2 / year in France
Total: 749 Mt CO2
in 2018
Electronics is here
but not only

## Slide 20: Agenda
Laws and Labels

## Slide 21: Goal & Disclaimer
Goal : overview of current Sustainable Products and Green IT legislations
Disclaimer: “IANAL” = I am not a lawyer

## Slide 22: EU Terms
Regulation = legislative act directly applicable in EU member states
  Does not require national implementing measures
  Enhance uniformity of law across all member states
  Example: GDPR (General Data Protection Regulation)
Directive = legislative act that sets the objectives/results that members must achieve
  Not directly applicable
  Members must transpose it into their national legal system before a deadline
  More flexible, adaptable to national context
  Example: EU single-use plastics directive
https://european-union.europa.eu/institutions-law-budget/law/types-legislation_en

## Slide 23: Product vs Product
Product in the sense of a new product line
  Life cycle: Development / Introduction / Maturity / Last order / Deprecation
Product in the sense of an object
  Life cycle: Manufacturing / Usage / Dispose
Current laws implements a object-based approach
Main limit: local optimization only

## Slide 24: Overview of a product life cycle
Impact
Time
1
2
4
5
6
3
1
Optimize manufacture
2
Increase energy efficiency
3
Increase reliability
4
Improve reparability
5
EOL management
6
Delay obsolescence
Inspired by : Écoconception en électronique de puissance. Impacts du dimensionnement, de la modularité et de la diagnosticabilité, Briac Baudais, 2024

## Slide 25: French laws

## Slide 26: REEN law
REEN Law, 2022 (Réduction de l’Empreinte Environnementale du Numérique)
  Loi n°2021-1485 promulguée le 15 novembre 2021 ainsi que son décret d'application du 29 juillet 2022
    integration of sustainability in education (education code)
    Digital eco-design framework: e.g. extend lifespan of terminals, encourage reuse, limit the use of infinite scrolling, increase transparency
    Corporate Social Responsibility (CSR / RSE): encourages reporting
  Target: local authorities, large companies & public sector
Notes: Framework: Arcep, Arcom, Ademe

## Slide 27: WEEE
WEEE (Waste from Electrical and Electronic Equipment)
  = DEEE in France (déchets d'équipements électriques et électroniques)
  A waste management chain
In France
  Directive 2002/96/CE du 27 janvier 2003 relative aux déchets d’équipements électriques et électroniques.
  directive 2012/19/UE du 4 juillet 2012 (dite directive DEEE II).
  directive 2002/95/CE du 27 janvier 2003 relative aux substances dangereuses contenues dans ces équipements (dite directive RoHS)
  directive 2011/65/UE du 8 juin 2011 (dite directive RoHS II)
  Setting up a principle of producer responsibility (REP)
Video on e-waste management

## Slide 28: Vigilance Law
Vigilance Law, 2017
  Loi n° 2017-399 relative au devoir de vigilance des sociétés mères et des entreprises donneuses d'ordre
    companies with more than 5,000 employees in France, or more than 10,000 employees worldwide must build, disclose, and implement a vigilance plan
    The vigilance plan must identify risks and prevent human rights violations and environmental damage
      resulting from the operations of the company
      resulting from the operations of its subcontractors.
Savourey, E., & Brabant, S. (2021). The French law on the duty of vigilance:
Theoretical and practical challenges since its adoption.
Business and Human Rights Journal, 6(1), 141-152.
Notes: Effondrement d’un Immeuble Bangladesh qui a tué >1000 personnes travaillant pour des sous-traitants de marques de fringues occidentales
La France est le premier pays a faire une loi.

## Slide 29: Loi AGEC
AGEC Law, 2020 (Loi anti-gaspillage pour une économie circulaire)
  Loi n° 2020-105 du 10 février 2020 / Anti-Waste Law for a Circular Economy
    move away from disposable plastic ;
    better inform consumers (reparability index);
    combat waste and promote solidarity-based re-use;
    act against programmed obsolescence;
    environmentally responsible production
  This regulatory framework is supplemented by decrees concerning:
    the procedure for registering and declaring EEEs in the national register
    the methods for processing WEEE
    the distinction between household and professional EEEs
    the contract between waste management operators and eco-organizations or the producer who has set up an individual system

## Slide 30: European Union laws

## Slide 31: European Green Deal
European Green Deal, 2019
Strategy to achieve a climate-neutral, sustainable, and competitive economy by 2050
> 175 directives & regulations

## Slide 32: ROHS directive
Restriction of Hazardous Substances in EEEs
  Purpose: prevent hazardous substances, ensure safer disposal of WEEE
  2002/95/CE: 6 materials
    Lead (Pb)
    Mercury (Hg)
    Cadmium (Cd)
    Hexavalent chromium (Cr6+)
    Polybrominated biphenyls (PBB)
    Polybrominated diphenyl ether (PBDE)
  2011/65/UE: + 4 materials
    Bis(2-ethylhexyl) phthalate (DEHP)
    Butyl benzyl phthalate (BBP)
    Dibutyl phthalate (DBP)
    Diisobutyl phthalate (DIBP)
  2017/2102/UE: extending application, address second market operations

## Slide 33: Electronics and Toxicity
A smartphone contains 53 metals.
with Au, Pd, Pt, and Cu, 82% of the metal value is recycled (6% of device weight), if the device is collected.
Recycling from smartphones at EOL is not economically feasible for e.g Co (disregarding batteries), Ga, Ge, In, Ta, and the rare earth elements.
Bookhagen, B., Bastian, D., Buchholz, P., Faulstich, M., Opper, C., Irrgeher, J., ... & Koeberl, C. (2020). Metallic resources in smartphones. Resources Policy, 68, 101750.
Notes: What is not recycled ends up in combustion ashes or wastewater sludge.

## Slide 34: The Example of Guiyu City E-waste Recycling Town
The level of chromium and lead in people’s blood is higher than in a reference Chinese population
Huang, Wenlong, Xiaoling Shi, and Kusheng Wu. "Human body burden of heavy metals and health consequences of Pb exposure in Guiyu, an E-waste recycling town in China." International Journal of Environmental Research and Public Health 18.23 (2021): 12428.

## Slide 35: CSRD
European Corporate Sustainability Reporting Directive (CSRD)
  EU directive, 1er Janvier 2024
  Target: companies of all sizes, with phased implementations
  Expands and strengthens requirements for sustainability reporting + standardize
  Double materiality: how sustainability affect their business and vice-versa
  Mandatory auditing: information must be independently audited
  Integration with Financial Reporting

## Slide 36: REACH
Regulation (EC) 1907/2006 of the Registration, Evaluation, Authorisation and Restriction of Chemicals
  Objective: ensure protection for human health & environment from chemicals
  Shifts the responsibility from chemical safety from authorities to the industry
  Electronic manufacturers must register chemicals they produce/import/use.
  Ensure chemicals are used safely and identify substances that may require further scrutiny
  Substances of very high concern (carcinogenic, toxic) require autorisation
  Some substances may be restricted
https://echa.europa.eu

## Slide 37: WEEE directive
WEEE Directive 2012/19/EU
  Goal: protect the environment and human health by reducing WEEE sent to landfill
  Producer are responsible for financing collection, treatment, recycling & disposal.
  Collection: achieve >65% of average weight
  Recovery: increase to 75-86% of collected WEEE
  Control of transboundary movements
  Treatment: minimum requirements for removal of substances and components

## Slide 38: Ecodesign directive
Ecodesign Directive 2009/125/EC
  Framework for setting mandatory ecodesign requirements for energy-related products
  Goal: improve environmental performance throughout their entire life cycle
Replaced by Regulation (EU) 2024/1781 - Ecodesign for Sustainable Products Regulation (ESPR)
  Framework to improve circularity, energy performance & sustainability of products
  No limited to energy-related products: textile, furniture, tyres, paint, electronics, etc.
  Alignment with European Green Deal
  Introduce Digital Product Passport (DPP)
  Producers bear the full cost of waste management

## Slide 39: Digital Product Passport (DPP)
Digital Product Passport (DPP)
  Digital record providing structured information about a product & its entire value chain
  From material extraction to end-of-life management
  Increase transparency, sustainability and circularity by making data accessible
  Include information on composition, environmental impact, how to repair, recycle, dispose

## Slide 40: Regulation (EU) 2023/1670
Regulation (EU) 2023/1670
  Applies from 20 juin 2025!
  Mandatory ecodesign requirements for smartphones (and dumb phones) & tablets
  Pursuant to Ecodesign Directive 2009/125/EC
  Software update for at least 5 years after end of sale
  Battery: 800 cycles before reaching 80% of initial capacity
  Spare parts available 7 years after end of sales
  Increase resistance, no performance manipulation, etc.
  Simplify repair
Notes: Pursuant = conformément

## Slide 41: Regulation (EU) 2023/1669
Regulation (EU) 2023/1669
  Energy labelling of phones & tablets
  Energy efficiency is not enough!
  + battery endurance
  + repairability
  + drop resistance
  + IP rating
Expected savings: 20B€ by 2030
  3%: electricity
  97%: longer lifespan
Notes: Pursuant = conformément

## Slide 42: Ecolabels
Ecolabels
EnergyStar : very strong energy constraints on EEEs
Electronic Product Environmental Assessment Tool (EPEAT)
  reduction/elimination of hazardous substances
  choice of environmentally-friendly components
  taking into account the end-of-life of equipment right from the design stage
  equipment durability
  energy saving
  recycling
  packaging...

## Slide 43: Agenda
Best Practices & State-of-the-Art – Electronics Eco-design

## Slide 44: Research and engineering needed
Life cycle analysis of products and services
Circular Economy - 3R: Repair, Reuse, Recycle
  and Reduce, Refurbish…
Better energy management and reliability
New technologies, processes and materials with low footprint
  PCB, IC, other components
Delayed obsolescence of hardware and software stack

## Slide 45: Repair, reuse, recycle

## Slide 46: 3R
Making a system more reparable may require more connectors
  That themselves require abiotic resources
Recycling will increase the impact of end-of-life (!)
  And sustainability improvements need to be evaluated reliably
Shorter cycles have lower cost
But they do have a cost

## Slide 47: Ecodesign Brezet-van Hemel Wheel (ADEME version)
@ New Concepts
Low tech, biomimicry
Cooperation and functional economy
Breathrough innovation (technical, commercial, organizational)
Product system level
7.Optimisation of system end-of-life
Reuse, Recycling (material recovery),
Organic valorization
Encourage disassembly / separability,
Facilitate collection
6. Optimisation of product lifetime
Facilitate / reduce cleaning,
Facilitate maintenance,
Facilitate repair, Limit the impact of consumables,
Improve modularity, Reduce obsolescence
(design, function, software), More robust design
5. Reduction of impacts during use
Inform to improve user behavior,
Reduction in usage consumption,
Encourage multifunctionality with
optimized or identical product
size/complexity/volume
(while questioning the need)
Product structure level
4. Optimisation of distribution system
Reduction/elimination of transport packaging (mass/volume),
Choice of less impactful transport packaging materials, Reusable transport packaging,
Reduction in the number of transports, Low-impact transport, Optimize the mass / volume of transport
3. Optimisation of production techniques
Reduction in energy consumption, High-performance sites
(renewable energies, water treatment plant, etc.),
Lower-impact technology/solution,
Reduction of manufacturing steps
Product component level
1. Supplies / Materials / Purchases with Lower Impact*
Supplier traceability, Recycled materials,
Recyclable materials, Bio-based materials,
Less toxic materials/solutions, Selection of materials,
High environmental performance (energy, water, etc.),
Local materials, Improve supply / packaging materials
2. Reduction of materials usage
Lightweighting, Reduction in the number of parts / materials,
Optimization of geometry/miniaturization/standardization,
Recovery/reduction of production waste,
Reduction of material quantity in product packaging
Notes: Risk : impact migration

## Slide 48: Ecodesign Brezet-van Hemel Wheel (ADEME version)
@ New Concepts
Low tech, biomimicry
Cooperation and functional economy
Breathrough innovation (technical, commercial, organizational)
Product system level
7.Optimisation of system end-of-life
Reuse, Recycling (material recovery),
Organic valorization
Encourage disassembly / separability,
Facilitate collection
6. Optimisation of product lifetime
Facilitate / reduce cleaning,
Facilitate maintenance,
Facilitate repair, Limit the impact of consumables,
Improve modularity, Reduce obsolescence
(design, function, software), More robust design
5. Reduction of impacts during use
Inform to improve user behavior,
Reduction in usage consumption,
Encourage multifunctionality with
optimized or identical product
size/complexity/volume
(while questioning the need)
Product structure level
4. Optimisation of distribution system
Reduction/elimination of transport packaging (mass/volume),
Choice of less impactful transport packaging materials, Reusable transport packaging,
Reduction in the number of transports, Low-impact transport, Optimize the mass / volume of transport
3. Optimisation of production techniques
Reduction in energy consumption, High-performance sites
(renewable energies, water treatment plant, etc.),
Low-impact technology/solution,
Reduction of manufacturing steps
Product component level
1. Supplies / Materials / Purchases with Lower Impact*
Supplier traceability, Recycled materials,
Recyclable materials, Bio-based materials,
Less toxic materials/solutions, Selection of materials,
High environmental performance (energy, water, etc.),
Local materials, Improve supply / packaging materials
2. Reduction of materials usage
Lightweighting, Reduction in the number of parts / materials,
Optimization of geometry/miniaturization/standardization,
Recovery/reduction of production waste,
Reduction of material quantity in product packaging
Circular economy
System lifetime extension

## Slide 49: The ESOS project
Electronics: Sustainable, Open and Sovereign
INSA Rennes, Université de Rennes, ENS Rennes
2023-2028, 6.3M€ funding, 15M€ total cost, funded by France2030
  Sustainable: meeting the needs of the present generation without compromising the ability of future generations to meet their own needs.
  Open: a decentralized development model that publicly distributes the source code for open collaboration and peer production, known as "the open-source method."
  Sovereign: the quality of a state being free and independent, determined solely by its own will within the limits of the higher principle of law, and in accordance with the collective purpose it is called to achieve.

## Slide 50: ESOS – 7 actions
Attract pupils to electronics
Train students to ESOS
  Licence, master, doctorate
Train teachers to ESOS
Train professionals to ESOS
  Trainings on eco-design : stay tuned!
Create open teaching material
https://esos.insa-rennes.fr
30+ industrial partners
14 PhD theses
Looking for synergies!

## Slide 51: ESOS – 14 PhDs
Digital systems ecodesign
Biosourced electronics
Low energy electronics
Low impact sensors and antennas
Energy harvesting
Brezet-van Hemel
Wheel
@New concepts
1 Novel materials
2 Less materials
3 Better production techniques
4 Better distribution
5 Better use
6 Better lifetime
7 Better end-of-life
Longer lifetime digital systems
Systems LCA

## Slide 52: Conclusion: LCA of electronics
Methods and tools for LCA are mature
  Databases for background, and tools for entering inputs flows and computing costs
The main challenges are
  Access to impact data
    Supply chain and industrial secrecy
  Unknowns at the time of LCA
    Location, Materials
LCA must be handled with care
  Never disclose data without assumptions
The state-of-the-art of LCA will evolve fast, with regulations
Notes: M. Ashby, Cambridge

## Slide 53: State-of-the-Art of Electronics Eco-design
Books to go further on LCA
  Mickaël Ashby
  Reinout Heijungs, et. al
  Michael Z. Hauschild, et. al
Conferences to go further on LCA of electronics
  Electronics goes Green, Fraunhofer IZM
  IEEE Sustainable Technologies
  Sustainability sessions in
    Design Automation and Test in Europe Conference 2023-25
    With proceedings : Digital System Design Conference 2024 (DSD 2024)
    With proceedings : Computing Frontiers 2025
    With proceedings : Design Automation and Test in Europe Conference 2026 (DATE 26)
More to be created!

## Slide 54: Thanks