## Slide 1: Strategies, Tools and Perspectives for Sustainable Electronics
RAPIDO 2024
Maxime Pelcat, INSA Rennes, Univ Rennes, IETR - UMR CNRS 6164

## Slide 2: Scope
What is the electronics market?
What are the sustainability challenges? (focus on environment)
How does electronics affect environment? (focus on climate)
How can we act towards sustainable electronics?

## Slide 3: Electronic devices
Electronic devices
  Collins dictionary: Electronics is the technology of using transistors and silicon chips, especially in devices such as radios, televisions, and computers.
Electrical devices
  Electrical devices functionally rely on electric energy (AC or DC) to drive their core parts (electric motors, transformers, rechargeable batteries…).
Both: EEE: Electrical and Electronic Equipments
Notes: Semiconductor: 600B today, 1T in 2030

## Slide 4: Electrical and Electronic Equipments (EEE)
Air purifier
Air conditioner
Alarm clock
Backup charger
Bread maker
Banknote counter
Blender
Bluetooth speaker
Bulb
Calculator
Car toy
Ceiling fan
Chandelier
Clock
Clothes dryer
Coffee maker
Computer
Copier
Curling iron
Digital camera
Dishwasher
Doorbell camera
Drill
Dvd player
Earphones
Electric frying pan
Electric grill
Electric guitar
Electric pencil sharpener
Electric razor
Exhaust fan
External hard drive
Fan
Facial cleansing machine
Fax
Fish tank
Floor lamp
Game controller
Garage
Grandfather clock
Hair dryer
Headset
Inkjet printer
iPod
Iron
Juicer
Kettle
Kitchen scale
Hair straightening machine
Laser printer
Lawn mower
Lift
Meat grinder
Microphone
Microwave
Mixer
Monitor
Mosquito racket
Mouse
Mp3 player
Oil-free fryer
Piano
Oven
Plotter
Pressure cooker
Printer
Projector
Radiator
Radio
Reading lamp
Refrigerator
Remote control
Rice cooker
Safe
Robotic vacuum cleaner
Sandwich maker
Scale
Scanner
Sewing machine
Smart television
Smartphone
Speakers
Tablet
Television
Timer
Toaster
Torch
USB drive
Vacuum cleaner
Walkie-talkie
Washing machine
Watch
Water pumps
Water purifier
Wall fan
Water heater
Webcam
Wifi modem
List from 7esl.com
Main Computing
Continuum devices

## Slide 5: Electrical and Electronic Equipments (EEE)
And
xG Base stations
Cars
Boats
Planes
Trains
Tramways
Busses
Windmills
Power plants
Satellites
Rockets
Supercomputers
Data centers
…
CC-BY NASA's James Webb Space Telescope from Greenbelt, MD, USA
CC-BY-SA Aynamankajan

## Slide 6: Electronic devices
CC-SA Project Kei
CC SA Angels Pinyol
Notes: Composants Chimiques, électromécaniques, électroniques

## Slide 7: Electronic devices
Sensors
Power Management
Actuators
Computing
Communication / Networking
Storage
Hardware Interface
Operating System
Libraries
Applications
Drivers
Electronic equipment
Electrical equipment
From another energy to electrical energy
From electrical energy to another energy

## Slide 8: Electronics market and Europe (in 2017)
Notes: Semiconductor: 600B today, 1T in 2030

## Slide 9: Human carbon impact
Human GHG emissions reach 60Gt/year
To respect the 1.5°C scenario of the Paris Agreement, emissions must reach 8Gt/year by 2050, i.e. a reduction of ~7× by 2050
The Closing Window: Climate crisis calls for rapid transformation of societies,
UN environment program 2022
8Gt

## Slide 10: Human carbon impact
Human GHG emissions reach 60Gt/year
To respect the 1.5°C scenario of the Paris Agreement, emissions must reach 8Gt/year by 2050, i.e. a reduction of ~7× by 2050
8Gt
Chart: 
| 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Série 1 | 59 | 55.165 | 51.5793 | 48.2266 | 45.0919 | 42.1609 | 39.4205 | 36.8581 | 34.4624 | 32.2223 | 30.1278 | 28.1695 | 26.3385 | 24.6265 | 23.0258 | 21.5291 | 20.1297 | 18.8213 | 17.5979 | 16.454 | 15.3845 | 14.3845 | 13.4495 | 12.5753 | 11.7579 | 10.9937 | 10.2791 | 9.6109 | 8.9862 | 8.4021 | 7.856 | 7.3453
-7%/year

## Slide 11: Human carbon impact per sector (in France)
Chart: 
| Transportation | Agriculture | Construction | Industry | Energy | Waste
Territorial emissions in France in 2018 (Mt CO2e) | 137 | 86 | 84 | 79 | 46 | 14
Suivi de la Stratégie Nationale Bas-Carbone
Indicateurs de résultats
Ministère de la Transition Ecologique, 2021

## Slide 12: Two strategies to distribute efforts
Chart: 
| Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible | Negligible
Territorial emissions | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01
Chart: 
| Transportation | Agriculture | Construction | Industry | Energy | Waste
Territorial emissions in France in 2018 (Mt CO2e) | 137 | 86 | 84 | 79 | 46 | 14
Chart: 
| Transportation | Agriculture | Construction | Industry | Energy | Waste
Territorial emissions in France in 2018 (Mt CO2e) | 137 | 86 | 84 | 79 | 46 | 14
1
2

## Slide 13: How does electronics affect environment?

## Slide 14: How do EEE help sustainability?
All energy transitions/shifts heavily employ electronics and electrical equipments (EEE)
  Electric cars, renewable energies from windmills, solar panel, heat pumps…
Energy optimization heavily relies on EEEs
  Smart grids, smart buildings, smart cities…
+
CC 3.0 ChristofferRiemer
CC SA Kritzolina

## Slide 15: How do EEE hinder sustainability?
(focusing on environmental impacts)
Production of EEEs
  Requires rare material (abiotic resource depletion)
  Emits greenhouse gases
  Requires much water
Usage of EEEs
  Requires energy
End-of-life of EEEs
  Emits about no greenhouse gases
  Emits e-wastes that pollute water and soils
-
Author: Laconicon

## Slide 16: Semiconductors and GHG emissions
85% of a cell phone's GHG emissions come from manufacturing
Gupta, U., Kim, Y. G., Lee, S., Tse, J., Lee, H. H. S., Wei, G. Y., ... & Wu, C. J. (2022).
Chasing carbon: The elusive environmental footprint of computing. IEEE Micro.

## Slide 17: Absolute carbon emissions of devices
Gupta, U., Kim, Y. G., Lee, S., Tse, J., Lee, H. H. S., Wei, G. Y., ... & Wu, C. J. (2022).
Chasing carbon: The elusive environmental footprint of computing. IEEE Micro.

## Slide 18: Semiconductors and GHG emissions
The manufacture of integrated circuits is the primary cause of cell phone emissions
Louis-Philippe, P. V. C., Jacquemotte, Q. E., & Hilty, L. M. (2020). Sources of variation in life cycle assessments of smartphones and tablet computers. Environmental Impact Assessment Review, 84

## Slide 19: Semiconductors and GHG emissions
Scope 1 emissions: F-gases
  F-gases are used for cleaning and etching, as well as for heat pumps and refrigerants
  1kg of SF6  23 tons of CO2, and lasts 3200 years in the atmosphere
Scope 2 emissions: electricity
  From 60g CO2e/kWh to 1kg CO2e/kWh
Bartos, S. C., & Burton, C. S. (2002). PFC, HFC, NF3, and SF6 emissions from semiconductor manufacturing. Good Practice Guidance and Uncertainty Management in National Greenhouse Gas Inventories, 1-13.
Notes: F-gases have replaced ozone-depleting gases

## Slide 20: Semiconductors and GHG emissions
Scope 3 upstream emissions
  Mining materials
  Smelting
  Refining
    High temperature processes for wafer production: reducing silicon from SiO2, purifying silicon, building single crystal silicon ingots
Scope 3 downstream emissions
  Transporting products
  Using products
  End-of-life
Impacts of electronics are increasingly well understood
Greenhouse Gas Protocol, World Resources Institute, Revised edition, 2015
Client
Notes: Ultrapure water, ultrapure silicium, coper, aluminum…

## Slide 21: Semiconductors and GHG emissions
The manufacture of integrated circuits emitted 76Mt CO2eq in 2021, an increase of 13% compared to 2020.
The current study excludes Scope 3.
Maxime Pelcat. GHG emissions of semiconductor manufacturing in 2021. Research Report. 2023. ⟨hal-04112708⟩

## Slide 22: Semiconductor industry revenue
Chart: 
| 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
Semiconductor revenues (B$) | 228.68 | 299.38 | 307.77 | 299.91 | 315.44 | 347.61 | 334.74 | 352.82 | 426.99 | 482.63 | 447.56 | 475.41 | 608.03 | 632.215
2030
1 trillion $
Numbers: Statista

## Slide 23: EEE-generated waste
E-waste
  One of the fastest-growing waste categories, growing at a rate of 3–5% per year  includes product housing
  In 2016, 44.7 million tons of e-waste were generated in the world , 6.1 kg per person; in 2019: 53.6 million tons
  “Only 17.4 per cent of 2019’s e-waste was collected and recycled.” Global E-waste Monitor 2020
CC BY-NC 3.0 IGO - © UNU/UNITAR and ITU, 2020
Ilankoon, I. M. S. K., Ghorbani, Y., Chong, M. N., Herath, G., Moyo, T., & Petersen, J. (2018).
E-waste in the international context – A review of trade flows, regulations, hazards,
waste management strategies and technologies for value recovery. Waste Management, 82, 258-275.

## Slide 24: How can we act?

## Slide 25: What is sustainable electronics?
Sustainable electronics is electronics that
  meets the needs of present generations without compromising the ability of future generations to meet their own needs.
  Brundtland report – “Our Common Future”, the United Nations, 1987
3 pilars
  Environmental
  Social
  Economic
Maslow’s pyramid

## Slide 26: Research needed!
Life cycle analysis of products and services
3R: Repair, Reuse, Recycle
  and Reduce, Refurbish…
Better energy management and reliability
New technologies, processes and materials with low footprint
  PCB, IC, other components
Delayed obsolescence of hardware and software stack
and all these at scale, with a valid business model

## Slide 27: Research needed!
Life cycle analysis of products and services
3R: Repair, Reuse, Recycle
  and Reduce, Refurbish…
Better energy management and reliability
New technologies, processes and materials with low footprint
  PCB, IC, other components
Delayed obsolescence of hardware and software stack

## Slide 28: From Local Decisions to Global Impacts
Communication
Transport
Healthcare
Defense
Industry
Energy
Agriculture
…
Human greenhouse gas emissions
Global Warming
Causality established and quantified by IPCC

## Slide 29: From Local Decisions to Global Impacts
Communication
Transport
Healthcare
Defense
Industry
Energy
Agriculture
…
Human greenhouse gas emissions
Global Warming
Causality established and quantified by IPCC
Causality to be established and quantified by domain experts

## Slide 30: LCA Method: ISO 14044 Standard
1- Goal and scope definition
2- Inventory analysis
3- Impact assessment
4- Interpretation / discussion
ISO 14040:2006, Environmental management — Life cycle assessment — Principles and framework

## Slide 31: Different forms of LCAs for different objectives
Gather reliable, scientific numbers on electronics impacts, and evaluate their reliability
  Attributional LCA: aims to describe the environmentally relevant physical flows to and from a life cycle
  Consequential LCA: LCA aiming to describe how environmentally relevant flows will change in response to possible decisions
Finnveden, G., Hauschild, M. Z., Ekvall, T., Guinée, J., Heijungs, R., Hellweg, S., ... & Suh, S. (2009). Recent developments in life cycle assessment. Journal of environmental management, 91(1), 1-21.

## Slide 32: Variations in semiconductor LCAs
Product lifecycle analysis is a complex science, requiring a detailed understanding of the scope and assumptions involved
Pirson, T., Delhaye, T. P., Pip, A., Le Brun, G., Raskin, J. P., & Bol, D. (2022). The environmental footprint of IC production: Review, analysis and lessons from historical trends. IEEE Transactions on Semiconductor Manufacturing.

## Slide 33: Evaluating when to replace systems by LCA
impact of upgrading to a new technology node
analysis of 2017 processor trends indicated that upgrading may require upwards of 10 years of service time to break even on energy
Kline Jr, D., Parshook, N., Ge, X., Brunvand, E., Melhem, R., Chrysanthis, P. K., & Jones, A. K. (2019). GreenChip: A tool for evaluating holistic sustainability of modern computing systems. Sustainable Computing: Informatics and Systems, 22, 322-332.
Notes: Team at uni Pittsburg and Uni Utah
To determine the overall energy cost of a system during its lifetime, a usage scenario must be considered consisting of the time the system is awake versus asleep (sleep ratio), when awake, how much it is active versus idle (activity ratio), and the time period it will be in service.
The break even time indicates the point
when a new system will reach the same energy consumption of
the system it will replace. This comparison assumes the manufac-
turing cost has already been invested for the original system. Thus,
it identiﬁes the upgrade time, when the energy for the new system
will be less than leaving the original system in service.

## Slide 34: Tools and challenges of electronics LCA
Open source tools exist for LCA: OpenLCA, Brightway…
Some challenges
Scope and functional unit definition (step 1)
  E.g. how to attribute impacts shared with other products?
Access to reliable data (life cycle inventory step 2)
  Computation of materials, processes and energy required to build and operate a product
  Measured, calculated, estimated, interpolated, extrapolated…
Comparison of different LCAs and decision making (step 4)
  “Comparing the results of different LCA or LCI studies is only possible if the assumptions and context of each study are equivalent.” ISO 14044
Multidisciplinary discipline: materials, architecture, business…
LCAs are costly

## Slide 35: Research needed!
Life cycle analysis of products and services
3R: Repair, Reuse, Recycle
  and Reduce, Refurbish…
Better energy management and reliability
New technologies, processes and materials with low footprint
  PCB, IC, other components
Delayed obsolescence of hardware and software stack

## Slide 36: Repair, reuse, recycle
Mobile phones have a lifetime of 2.5 years, high-end processors 4.5 years
To be a leader in future chips, EU shall invest in novel lengthened lifetime chips and systems
  tools: upgradeable, reparable, reconfigurable, and repurposable chip and board technologies
  Build technologies for validating and providing warranty for reused components
  Eco-design and eco-innovation

## Slide 37: Repair, reuse, recycle
Making a system more reparable may require more connectors
  That themselves require abiotic resources
Recycling will increase the impact of end-of-life (!)
  And sustainability improvements need to be evaluated reliably
Shorter cycles have lower cost
But they do have a cost

## Slide 38: Repair, reuse, recycle
Europe acts already through new requirements

## Slide 39: LCAs: 16 evaluated impacts
Climate change
Ozone depletion
Human toxicity, cancer
Human toxicity, non-cancer
Particulate matter
Ionizing radiation, human health
Photochemical ozone formation, human health
Acidification
Eutrophication, terrestrial
Eutrophication, freshwater
Eutrophication, marine
Ecotoxicity, freshwater
Land use
Water use
Resource use, minerals and metals
Resource use, fossils

## Slide 40: Research needed!
Life cycle analysis of products and services
3R: Repair, Reuse, Recycle
  and Reduce, Refurbish…
Better energy management and reliability
New technologies, processes and materials with low footprint
  PCB, IC, other components
Delayed obsolescence of hardware and software stack

## Slide 41: Research needed!
Life cycle analysis of products and services
3R: Repair, Reuse, Recycle
  and Reduce, Refurbish…
Better energy management and reliability
New technologies, processes and materials with low footprint
  PCB, IC, other components
Delayed obsolescence of hardware and software stack

## Slide 42: New technologies, processes and materials
Organic electronics, bio-sourced PCBs…
Beware the rebound effect (!)
  Requires an evaluation of the large-scale impact of products

## Slide 43: Research needed!
Life cycle analysis of products and services
3R: Repair, Reuse, Recycle
  and Reduce, Refurbish…
Better energy management and reliability
New technologies, processes and materials with low footprint
  PCB, IC, other components
Delayed obsolescence of hardware and software stack

## Slide 44: The role of open source hardware
Code, application and library obsolescence is to be delayed
Open source hardware can stabilise interfaces and delay obsolescence :
  Instruction Set Architecture
  Application Binary Interface
  Device Tree Support
Carbon footprint reduction requires properties of open source communities
  Transparency
  Sharing information

## Slide 45: The ESOS project
Electronics: Sustainable, Open and Sovereign
2023-2028, 6.3M€ funding, 15M€ total cost, funded by France2030
  Sustainable: meeting the needs of the present generation without compromising the ability of future generations to meet their own needs.
  Open: a decentralized development model that publicly distributes the source code for open collaboration and peer production, known as "the open-source method."
  Sovereign: the quality of a state being free and independent, determined solely by its own will within the limits of the higher principle of law, and in accordance with the collective purpose it is called to achieve.

## Slide 46: ESOS – 7 actions
Attract pupils to electronics
Train students to ESOS
  Licence, master, doctorate
Train teachers to ESOS
Train professionals to ESOS
Create open teaching material
https://esos.insa-rennes.fr
30 industrial partners
14 PhD theses
Looking for synergies!

## Slide 47: Wrapping up: how can we act?
Propose new technologies for lower impact, repairable, reusable, reconfigurable, repurposable systems
Assess the real impact of these new technologies in the field with Life Cycle Analysis
Help and foster the setup of novel regulations (incentives, taxes and quotas)
Train students and professionals
Ashby, M. F. (2022). Materials and sustainable development. Butterworth-Heinemann.
Notes: M. Ashby, Cambridge

## Slide 48: Thanks!
CC-SA Project Kei
CC SA Angels Pinyol

## Slide 49: Additional Slides

## Slide 50: Electronics, ethics and human rights
Sustainability challenges in terms of social responsibility and human rights include:
  Social standards for employees
  Impacts on local communities
  Impact on society
Downstream
Upstream
Client

## Slide 51: LCAs: 16 evaluated impacts
Climate change
Ozone depletion
Human toxicity, cancer
Human toxicity, non-cancer
Particulate matter
Ionizing radiation, human health
Photochemical ozone formation, human health
Acidification
Eutrophication, terrestrial
Eutrophication, freshwater
Eutrophication, marine
Ecotoxicity, freshwater
Land use
Water use
Resource use, minerals and metals
Resource use, fossils