## Slide 1: Sustainable Electronics: Open Challenges and Opportunities
Maxime PELCAT,
IETR, INSA Rennes
2023
Credit: James Mathews - CC BY-SA 4.0
shared under the
CC BY-SA 2.0 FR licence
authors: Maxime Pelcat,
ESOS project

## Slide 2: Introduction: What is Sustainable Electronics?

## Slide 3: What is electronics?
Electronic devices
  Collins dictionary: Electronics is the technology of using transistors and silicon chips, especially in devices such as radios, televisions, and computers.
Electrical device
  Electrical devices functionally rely on electric energy (AC or DC) to drive their core parts (electric motors, transformers, lighting, rechargeable batteries…).
Both: EEE: Electrical and Electronic Equipment

## Slide 4: Electrical and Electronic Equipments
Air purifier
Air conditioner
Alarm clock
Backup charger
Bread maker
Banknote counter
Blender
Bluetooth speaker
Bulb
Calculator
Car toy
Ceiling fan
Chandelier
Clock
Clothes dryer
Coffee maker
Computer
Copier
Curling iron
Digital camera
Dishwasher
Doorbell camera
Drill
Dvd player
Earphones
Electric frying pan
Electric grill
Electric guitar
Electric pencil sharpener
Electric razor
Exhaust fan
External hard drive
Fan
Facial cleansing machine
Fax
Fish tank
Floor lamp
Game controller
Garage
Grandfather clock
Hair dryer
Headset
Inkjet printer
iPod
Iron
Juicer
Kettle
Kitchen scale
Hair straightening machine
Laser printer
Lawn mower
Lift
Meat grinder
Microphone
Microwave
Mixer
Monitor
Mosquito racket
Mouse
Mp3 player
Oil-free fryer
Piano
Oven
Plotter
Pressure cooker
Printer
Projector
Radiator
Radio
Reading lamp
Refrigerator
Remote control
Rice cooker
Safe
Robotic vacuum cleaner
Sandwich maker
Scale
Scanner
Sewing machine
Smart television
Smartphone
Speakers
Tablet
Television
Timer
Toaster
Torch
USB drive
Vacuum cleaner
Walkie-talkie
Washing machine
Watch
Water pumps
Water purifier
Wall fan
Water heater
Webcam
Wifi modem
List from 7esl.com
Notes: Air purifier
Air conditioner
Alarm clock
Backup charger
Bread maker
Banknote counter
Blender
Bluetooth speaker
Bulb
Calculator
Car toy
Ceiling fan
Chandelier
Clock
Clothes dryer
Coffee maker
Computer
Copier
Curling iron
Digital camera
Dishwasher
Doorbell camera
Drill
Dvd player
Earphones
Electric frying pan
Electric grill
Electric guitar
Electric pencil sharpener
Electric razor
Electric stove
Exhaust fan
External hard drive
Fan
Facial cleansing machine
Fax
Fish tank
Floor lamp
Game controller
Garage
Grandfather clock
Hair dryer
Headset
Inkjet printer
iPod
Iron
Juicer
Kettle
Kitchen scale
Hair straightening machine
Laser printer
Lawn mower
Lift
Meat grinder
Microphone
Microwave
Mixer
Monitor
Mosquito racket
Mouse
Mp3 player
Oil-free fryer
Piano
Oven
Plotter
Pressure cooker
Printer
Projector
Radiator
Radio
Reading lamp
Refrigerator
Remote control
Rice cooker
Safe
Robotic vacuum cleaner
Sandwich maker
Scale
Scanner
Sewing machine
Smart television
Smartphone
Speakers
Tablet
Television
Timer
Toaster
Torch
USB drive
Vacuum cleaner
Walkie-talkie
Washing machine
Watch
Water pumps
Water purifier
Wall fan
Water heater
Webcam
Wifi modem

## Slide 5: Electrical and Electronic Equipments
Air purifier
Air conditioner
Alarm clock
Backup charger
Bread maker
Banknote counter
Blender
Bluetooth speaker
Bulb
Calculator
Car toy
Ceiling fan
Chandelier
Clock
Clothes dryer
Coffee maker
Computer
Copier
Curling iron
Digital camera
Dishwasher
Doorbell camera
Drill
Dvd player
Earphones
Electric frying pan
Electric grill
Electric guitar
Electric pencil sharpener
Electric razor
Exhaust fan
External hard drive
Fan
Facial cleansing machine
Fax
Fish tank
Floor lamp
Game controller
Garage
Grandfather clock
Hair dryer
Headset
Inkjet printer
iPod
Iron
Juicer
Kettle
Kitchen scale
Hair straightening machine
Laser printer
Lawn mower
Lift
Meat grinder
Microphone
Microwave
Mixer
Monitor
Mosquito racket
Mouse
Mp3 player
Oil-free fryer
Piano
Oven
Plotter
Pressure cooker
Printer
Projector
Radiator
Radio
Reading lamp
Refrigerator
Remote control
Rice cooker
Safe
Robotic vacuum cleaner
Sandwich maker
Scale
Scanner
Sewing machine
Smart television
Smartphone
Speakers
Tablet
Television
Timer
Toaster
Torch
USB drive
Vacuum cleaner
Walkie-talkie
Washing machine
Watch
Water pumps
Water purifier
Wall fan
Water heater
Webcam
Wifi modem
List from 7esl.com
Main EEE devices
of digital society
Notes: Air purifier
Air conditioner
Alarm clock
Backup charger
Bread maker
Banknote counter
Blender
Bluetooth speaker
Bulb
Calculator
Car toy
Ceiling fan
Chandelier
Clock
Clothes dryer
Coffee maker
Computer
Copier
Curling iron
Digital camera
Dishwasher
Doorbell camera
Drill
Dvd player
Earphones
Electric frying pan
Electric grill
Electric guitar
Electric pencil sharpener
Electric razor
Electric stove
Exhaust fan
External hard drive
Fan
Facial cleansing machine
Fax
Fish tank
Floor lamp
Game controller
Garage
Grandfather clock
Hair dryer
Headset
Inkjet printer
iPod
Iron
Juicer
Kettle
Kitchen scale
Hair straightening machine
Laser printer
Lawn mower
Lift
Meat grinder
Microphone
Microwave
Mixer
Monitor
Mosquito racket
Mouse
Mp3 player
Oil-free fryer
Piano
Oven
Plotter
Pressure cooker
Printer
Projector
Radiator
Radio
Reading lamp
Refrigerator
Remote control
Rice cooker
Safe
Robotic vacuum cleaner
Sandwich maker
Scale
Scanner
Sewing machine
Smart television
Smartphone
Speakers
Tablet
Television
Timer
Toaster
Torch
USB drive
Vacuum cleaner
Walkie-talkie
Washing machine
Watch
Water pumps
Water purifier
Wall fan
Water heater
Webcam
Wifi modem

## Slide 6: And Other Electrical and Electronic Equipments
And
xG Base stations
Cars
Boats
Planes
Trains
Tramways
Busses
Windmills
Power plants
Satellites
Rockets
Supercomputers
Data centers
…
Notes: Air purifier
Air conditioner
Alarm clock
Backup charger
Bread maker
Banknote counter
Blender
Bluetooth speaker
Bulb
Calculator
Car toy
Ceiling fan
Chandelier
Clock
Clothes dryer
Coffee maker
Computer
Copier
Curling iron
Digital camera
Dishwasher
Doorbell camera
Drill
Dvd player
Earphones
Electric frying pan
Electric grill
Electric guitar
Electric pencil sharpener
Electric razor
Electric stove
Exhaust fan
External hard drive
Fan
Facial cleansing machine
Fax
Fish tank
Floor lamp
Game controller
Garage
Grandfather clock
Hair dryer
Headset
Inkjet printer
iPod
Iron
Juicer
Kettle
Kitchen scale
Hair straightening machine
Laser printer
Lawn mower
Lift
Meat grinder
Microphone
Microwave
Mixer
Monitor
Mosquito racket
Mouse
Mp3 player
Oil-free fryer
Piano
Oven
Plotter
Pressure cooker
Printer
Projector
Radiator
Radio
Reading lamp
Refrigerator
Remote control
Rice cooker
Safe
Robotic vacuum cleaner
Sandwich maker
Scale
Scanner
Sewing machine
Smart television
Smartphone
Speakers
Tablet
Television
Timer
Toaster
Torch
USB drive
Vacuum cleaner
Walkie-talkie
Washing machine
Watch
Water pumps
Water purifier
Wall fan
Water heater
Webcam
Wifi modem

## Slide 7: Concentrating on Electronics

## Slide 8: What is sustainable electronics?
Sustainable electronics is electronics that
  meets the needs of present generations without compromising the ability of future generations to meet their own needs.
  Brundtland report – “Our Common Future”, the United Nations, 1987
What are the needs of current generation?
How do we compromise the needs of future generations?

## Slide 9: Brundtland Report
Chapter 2: Towards Sustainable Development
81. the pursuit of sustainable development requires:
  a political system that secures effective citizen participation in decision making,
  an economic system that is able to generate surpluses and technical knowledge on a self-reliant and sustained basis,
  a social system that provides for solutions for the tensions arising from disharmonious development,
  a production system that respects the obligation to preserve the ecological base for development,
  a technological system that can search continuously for new solutions,
  an international system that fosters sustainable patterns of trade and finance, and an administrative system that is flexible and has the capacity for self-correction.
82. These requirements are more in the nature of goals that should underlie national and international action on development. What matters is the sincerity with which these goals are pursued and the effectiveness with which departures from them are corrected.
Notes: Gro Harlem Brundtland
Ancienne Première ministre de Norvège

## Slide 10: Claims on sustainable electronics
Researchers and teacher are key players to reach sustainable electronics
To progress towards sustainability, we shall
  Employ verified, scientific information
  Go beyond extreme positions
  Pinpoint the problems and the potential solutions
  Incorporate engineering and social sciences
  Pursue the goal with sincerity
  Share information and question the method
Open source hardware has a major role to play

## Slide 11: Outline
Electronics and Sustainability Challenges
  How is electronics designed and built?
  Focus on global warming
How to act on electronics sustainability?
  Low energy, life cycle analysis, product extended lifetimes and the role of open source hardware
  Focus on the ESOS project

## Slide 12: Electronics and Sustainability Challenges

## Slide 13: Electronics and Innovation
Electronics support most innovations in
  Communication, Mobility, Health, Energy, Industry, Farming
In particular, digital technologies help:
  Improved social connectivity
  Improved communication speeds
  Enhanced learning opportunities
  Improved versatile working
  Automation of tasks
  Information storage
  Information editing

## Slide 14: Understanding sustainability
UN 17 sustainable development goals for 2030

## Slide 15: How do EEE help sustainability?
All energy transitions/shifts heavily employ EEEs
  Electric cars, renewable energies from windmills, solar panel, heat pumps…
Energy reduction heavily relies on EEEs
  Smart grids, smart buildings, smart cities…
More largely, production optimization and earth observation heavily rely on EEEs
  Precision farming, earth observation satellites…
+
CC 3.0 ChristofferRiemer
CC SA Kritzolina

## Slide 16: How do EEE hinder sustainability?
(Apart from social and economical impacts)
Production of EEEs
  Requires rare material which mining emits greenhouse gases and wastes
  Emits greenhouse gases
  Requires much water
Usage of EEEs
  Produces heat
  Requires energy
End-of-life of EEEs
  Emits e-wastes that pollute water and soils
-

## Slide 17: How is electronics Designed and Built?

## Slide 18: Examples: Printed Circuit Boards
CC BY-SA Maxime Pelcat
Notes: Les stratifiés sont fabriqués en durcissant sous pression et température des couches fibreuses (fibre de verre, papier, etc.) avec une matrice, le plus souvent de la résine époxyde thermodurcie. Cela forme une pièce finale d'épaisseur uniforme dont les plaques carrées peuvent mesurer jusqu'à 2,5 m de côté. L'épaisseur et les caractéristiques diélectriques du circuit sont données par différents tissages, concentration et épaisseur de fibres, et par le pourcentage résine/fibre.
thermoset epoxy resin + copper wires

## Slide 19: Examples: Electronics Components
Notes: Chemical, semiconductor, mechanical, mixed (e.g. MEMs)

## Slide 20: Examples: Communications and storage

## Slide 21: Examples: Smartphones
CC BY-SA Vera de Kok

## Slide 22: Examples: PC power supply

## Slide 23: Structure of an embedded system
Sensors
Power Management
Actuators
Computing
Communication / Networking
Storage
Hardware
Operating System
Libraries
Applications
Drivers

## Slide 24: Supply chain (in general)
Industry employs a supply chain pyramid with Tiers
…
OEM: Original Equipment Manufacturer
TIER 1: Module or system supplier
TIER 2: Component supplier
TIER 3: Sub-component supplier
TIER N: Natural resource supplier
Flaticons: Mehwish, Freepik

## Slide 25: The electronics industry supply chain
Industry employs a supply chain pyramid with Tiers
…
OEM: Original Equipment Manufacturer
TIER 1: PCB supplier
TIER 2: Integrated circuit supplier
TIER 3: wafer supplier
TIER N: Minerals supplier
Flaticons: Surang, Kerismaker, Freepik, smashicons

## Slide 26: What is an integrated circuit?
Digital ICs
  Processor
    Large microprocessor
    Small microcontroller
    Specialized processors (telecommunications, cameras, …)
  Memory (data storage): ROM, RAM
Analog ICs
  Amplifier, sensor, MEMS (Micro Electro Mechanical System)
  Power integrated circuit
Mixed signals ICs
  Radio Frequency IC…

## Slide 27: +/- Impacts of electronics
Electronics has + and – effects at all levels of the Maslow’s hierarchy of needs

## Slide 28: Electronics, ethics and human rights
Challenges include:
  Social standards for employees
    Safe and healthy working conditions
    Freedom of association and right to collective bargaining
    Equality of opportunity and treatment and fair interaction
    Remuneration
    Working hours
    Employment security
    Social security
    Professional development
    Job satisfaction
  Impacts on local communities
  Impact on society

## Slide 29: Electronics, ethics and human rights
Challenges include:
  Social standards for employees
  Impacts on local communities
    Safe and healthy living
    Human rights
    Social and economic opportunities
  Impact on society

## Slide 30: Electronics, ethics and human rights
Challenges include:
  Social standards for employees
  Impacts on local communities
  Impact on society
    Unjustifiable risks
    Employment creation
    Corruption
    Contribution to the national economy
    Contribution to the national budget
    Impacts on conflicts
    Intellectual property rights

## Slide 31: Electronics and pollution
Smartphones: 55 elements employed
Ashby, M. F. (2022). Materials and sustainable development. Butterworth-Heinemann.

## Slide 32: E-Waste
CC BY-NC 3.0 IGO - © UNU/UNITAR and ITU, 2020

## Slide 33: E-Waste
E-waste
  One of the fastest-growing waste categories, growing at a rate of 3–5% per year  includes product housing
  In 2016, 44.7 million tons of e-waste were generated in the world , 6.1 kg per person; in 2019: 53.6 million tons
  E-waste is classified as a hazardous waste.
    “Only 17.4 per cent of 2019’s e-waste was collected and recycled. This means that gold, silver, copper, platinum and other high-value, recoverable materials conservatively valued at US $57 billion – a sum greater than the Gross Domestic Product of most countries – were mostly dumped or burned rather than being collected for treatment and reuse.” - Global E-waste Monitor 2020
Ilankoon, I. M. S. K., Ghorbani, Y., Chong, M. N., Herath, G., Moyo, T., & Petersen, J. (2018).
E-waste in the international context–A review of trade flows, regulations, hazards,
waste management strategies and technologies for value recovery. Waste Management, 82, 258-275.

## Slide 34: Focus on Global Warming

## Slide 35: Global Warming, in France
Aurélien Ribes et al. 2022, « Earth Syst. Dynam. », 13, 1397-1415 (CC BY-4.0)
Prediction for an intermediate scenario in which carbon emissions
neither increase nor decrease drastically
Notes: Dans un deuxième temps, les chercheurs se sont projetés vers l’avenir afin d’anticiper le climat français à la fin du XXIe siècle. Ils ont pour cela utilisé les simulations climatiques en fonction de différents scénarios décrivant l’état du monde en 2100. Ces scénarios construits par le Giec vont du plus optimiste – un monde dans lequel un immense effort international a permis d’atteindre la neutralité carbone dès 2050 – au plus pessimiste – un monde divisé par de fortes inégalités et qui continue à carburer au gaz, pétrole et charbon. Entre ces deux extrêmes improbables, un scénario intermédiaire dans lequel les émissions de carbone n’augmentent ni ne diminuent drastiquement. D’après les experts, c’est ce scénario mitigé qui est le plus en accord avec les tendances actuelles et les engagements climatiques pris par les grands pays émetteurs pour les prochaines années.
Sur la base de ce dernier scénario, les chercheurs ont montré que la France de 2100 pourrait être 3,8 °C plus chaude que celle du début du XXe siècle. Une augmentation qui fait frémir. Une telle hausse des températures serait particulièrement marquée en été. En effet, les étés pourraient être en moyenne 5 °C plus chauds par rapport aux décennies 1900-1930. « Ceci aura des impacts très forts sur les écosystèmes et les cultures. On aura des pics de chaleur beaucoup plus fréquents et chauds, et des sécheresses plus intenses et prolongées. Dans ces conditions, l’un de points clés sera comment maintenir les ressources en eau et comment les utiliser », annonce Julien Boé. À 3,8 °C de hausse de températures moyennes, des écosystèmes entiers pourraient disparaître, et le paysage agricole en sera drastiquement modifié.

## Slide 36: Data and Actions in France
Commission de l'aménagement du territoire et du développement durable du Sénat
  rapport de la mission d'information sur l'empreinte environnementale du numérique, 2019
  if nothing is done, by 2040 digital technology would be the source of 24 million tons of CO2 equivalent, or about 7% of France's emissions, compared with 2% today.

## Slide 37: Goal on global warming
Scenario below 1.5°C (66% chance in 2100 with no or limited overshoot): 8 GtCO2e in 2050 (gain of ~7×)
The Closing Window:Climate crisis calls for rapid transformation of societies
UN environment programme 2022
IPCC
Notes: For 1.5°C objective, Paris Agreement
Other studies estimate the safe level of greenhouse gas concentrations between 350 ppm and 400 ppm of CO2-equivalent.
Total emissions from global livestock: 7.1 Gigatonnes of Co2-equiv per year, representing 14.5 percent of all anthropogenic GHG emissions.
https://www.oecd.org/tax/tax-policy/pricing-greenhouse-gas-emissions-turning-climate-targets-into-climate-action.htm
Land Use, Land-Use Change and Forestry (LULUCF)

## Slide 38: Goal on global warming
In developed countries, reductions shall be stronger: estimated 6× in France in 2050
Notes: For 1.5°C objective, Paris Agreement
Other studies estimate the safe level of greenhouse gas concentrations between 350 ppm and 400 ppm of CO2-equivalent.
Total emissions from global livestock: 7.1 Gigatonnes of Co2-equiv per year, representing 14.5 percent of all anthropogenic GHG emissions.
https://www.oecd.org/tax/tax-policy/pricing-greenhouse-gas-emissions-turning-climate-targets-into-climate-action.htm
Land Use, Land-Use Change and Forestry (LULUCF)

## Slide 39: The case of global warming
All human activities produce CO2
Mt CO2 / year in France
Total: 749 Mt CO2
in 2018

## Slide 40: The case of global warming
All human activities produce CO2
Mt CO2 / year in France
Total: 749 Mt CO2
in 2018
Electronics is here

## Slide 41: The case of global warming
All human activities produce CO2
Mt CO2 / year in France
Total: 749 Mt CO2
in 2018
Electronics is here
but not only

## Slide 42: Carbon accounting
Greenhouse Gas Protocol and ISO 14064
  Employing an accounting method for carbon emission tracking (in tons of CO2 equivalent) to avoid double counting
  Scope 1: GHG direct emissions from activity
  Scope 2: GHG emissions from energy consumption
    Location-based: reflects the average emissions intensity of grids on which energy consumption occurs
    Market-based: taking into account, derives emission factors from contractual instruments (e.g. REC)
      renewable energy certificates (RECs)
  Scope 3: Indirect emissions from value chain (up and downstream)

## Slide 43: The electronics industry supply chain
Upstream and downstream
OEM: Original Equipment Manufacturer
TIER 1: PCB supplier
TIER 2: Integrated circuit supplier
TIER 3: wafer supplier
TIER N: Minerals supplier
Flaticons: Surang, Kerismaker, Freepik, smashicons, Muhammad Atif,
Distribution
Retail store
Downstream
Upstream
Client

## Slide 44: Electronics Life Cycle (LC)
Raw Materials
Manufacturing
Product (Consumer)
End-of-life
Collection
Recycling
Nature
Disposal
Nature
opex
Gupta, U., Kim, Y. G., Lee, S., Tse, J., Lee, H. H. S., Wei, G. Y., ... & Wu, C. J. (2022).
Chasing carbon: The elusive environmental footprint of computing. IEEE Micro, 42(4), 37-47.

## Slide 45: Electronics LC is strongly impacted by capex
Raw Materials
Manufacturing
Product (Consumer)
End-of-life
Collection
Recycling
Nature
Disposal
Nature
capex
Gupta, U., Kim, Y. G., Lee, S., Tse, J., Lee, H. H. S., Wei, G. Y., ... & Wu, C. J. (2022).
Chasing carbon: The elusive environmental footprint of computing. IEEE Micro, 42(4), 37-47.

## Slide 46: Electronics LC is strongly impacted by capex
Raw Materials
Manufacturing
Product (Consumer)
End-of-life
Collection
Recycling
Nature
Disposal
Nature
capex
Gupta, U., Kim, Y. G., Lee, S., Tse, J., Lee, H. H. S., Wei, G. Y., ... & Wu, C. J. (2022).
Chasing carbon: The elusive environmental footprint of computing. IEEE Micro, 42(4), 37-47.

## Slide 47: Electronics LC is strongly impacted by capex
Raw Materials
Manufacturing
Product (Consumer)
End-of-life
Collection
Recycling
Nature
Disposal
Nature
capex
Gupta, U., Kim, Y. G., Lee, S., Tse, J., Lee, H. H. S., Wei, G. Y., ... & Wu, C. J. (2022).
Chasing carbon: The elusive environmental footprint of computing. IEEE Micro, 42(4), 37-47.

## Slide 48: Electronics LC is strongly impacted by capex
Gupta, U., Kim, Y. G., Lee, S., Tse, J., Lee, H. H. S., Wei, G. Y., ... & Wu, C. J. (2022).
Chasing carbon: The elusive environmental footprint of computing. IEEE Micro, 42(4), 37-47.

## Slide 49: Electronics LC is strongly impacted by capex
Gupta, U., Kim, Y. G., Lee, S., Tse, J., Lee, H. H. S., Wei, G. Y., ... & Wu, C. J. (2022).
Chasing carbon: The elusive environmental footprint of computing. IEEE Micro, 42(4), 37-47.

## Slide 50: Semiconductor industry GHG accounting
Chart: Semiconductors main suppliers revenue in 2021
| Samsung Electronics | Intel | SK Hynix | Micron Technology | Qualcomm | Broadcom | MediaTek | Texas Instruments | Western Digital | Nvidia | AMD | STMicroelectronics | Kioxia | Infineon | NXP | Others
 | 73.2 | 72.54 | 36.35 | 28.62 | 27.09 | 18.79 | 17.62 | 17.27 | 16.92 | 16.82 | 16.3 | 12.76 | 12.1 | 11.06 | 11.06 | 219.53
36% = 219,53 
2021
Sources: companies CSR
Others are extrapolated from total market size

## Slide 51: Scope 1: direct impact
Chart: Semiconductor Fabrication Scope 1
| Samsung Electronics | Intel | SK Hynix (memories) | Micron Technology | Qualcomm | Broadcom | MediaTek | Texas Instruments | Western Digital | Nvidia | AMD | STMicroelectronics | Kioxia (Toshiba Memory) | Infineon | NXP | Others
Scope 1 2020 | 1602400.7678 | 1980000 | 2711409 | 3281887 | 112479 | 114096 | 4518 | 938506 | 44643 | 2817 | 2335 | 486000 | 651900 | 229890 | 195181 | 6983179.6651
Scope 1 2021 | 2379723.588 | 2190000 | 2628921 | 3459483 | 106659 | 126891 | 5326 | 1040450 | 46152 | 2692 | 2892 | 481000 | 694000 | 298246 | 240370 | 7743055.1113
2021
Sources: companies CSR
Samsung electronics GHG emissions are counted only for 31.3% (percentage of semiconductor in company revenues)
Others are extrapolated from market share

## Slide 52: Scope 1: direct impact
Chart: Semiconductor Fabrication Scope 1
| Samsung Electronics | Intel | SK Hynix (memories) | Micron Technology | Qualcomm | Broadcom | MediaTek | Texas Instruments | Western Digital | Nvidia | AMD | STMicroelectronics | Kioxia (Toshiba Memory) | Infineon | NXP | Others
Scope 1 2020 | 1602400.7678 | 1980000 | 2711409 | 3281887 | 112479 | 114096 | 4518 | 938506 | 44643 | 2817 | 2335 | 486000 | 651900 | 229890 | 195181 | 6983179.6651
Scope 1 2021 | 2379723.588 | 2190000 | 2628921 | 3459483 | 106659 | 126891 | 5326 | 1040450 | 46152 | 2692 | 2892 | 481000 | 694000 | 298246 | 240370 | 7743055.1113
fabless
fabless

## Slide 53: Scope 2: impact from energy
Chart: Semiconductor fabrication scope 2
| Samsung Electronics | Intel | SK Hynix (memories) | Micron Technology | Qualcomm | Broadcom | MediaTek | Texas Instruments | Western Digital | Nvidia | AMD | STMicroelectronics | Kioxia (Toshiba Memory) | Infineon | NXP | Others
Scope 2 2020 | 4917181.9578 | 3700000 | 4836919 | 3859402 | 203047 | 128076 | 52072 | 1195111 | 1000814 | 74692 | 47797 | 564000 | 1713400 | 737024 | 622741 | 13365210.7092
Scope 2 2021 | 6313277.7409 | 3820000 | 5302908 | 3961500 | 171932 | 187519 | 61992 | 1262328 | 929882 | 105621 | 38956 | 473000 | 1848000 | 924168 | 659363 | 14725997.0992
Sources: companies CSR
Location-based scope 2 if available, otherwise market-based or non specified (marked with *)
*
*
*
*
*
*
*
*
fabless
fabless

## Slide 54: Foundries carbon impact
Chart: 
| TSMC | UMC (United Microelectronics Corporation) | Globalfoundries | SMIC (Semiconductor Manufacturing International Corporation) | Others | TW | TW | US | CN | -
Foundries : In scope 3 of others | 56.82 | 7.62 | 6.59 | 5.44 | 6.6496
2021

## Slide 55: Foundries scope 1
Chart: 
| TSMC | UMC (United Microelectronics Corporation) | Globalfoundries | SMIC (Semiconductor Manufacturing International Corporation) | Others | TW | TW | US | CN | -
 | 10304344 | 498907 | 467894 | 680308 | 1039256.7826
2021

## Slide 56: Foundries scope 2
Chart: 
| TSMC | UMC (United Microelectronics Corporation) | Globalfoundries | SMIC (Semiconductor Manufacturing International Corporation) | Others | TW | TW | US | CN | -
 | 9196964 | 1298439 | 215810 | 1558785 | 1066956.3478
2021

## Slide 57: Some details on scope 1 emissions
Semiconductor industry heavily use F-Gases
  HFC (hydrofluorocarbons): cooling
  PFC (perfluorocarbons): etching and cleaning
  SF6: 1kG = 22.8t CO2eq
Chart: Full Samsung Electronics Scope 1 emissions in ktons CO2
| CO2 | CH4 | N2O | HFCs | PFCs | SF6
ktons CO2 | 11005 | 3 | 489 | 902 | 4787 | 214

## Slide 58: Semiconductor GHG accounting
Scope 1+2: 88Mt CO2eq in 2021
  +10% GHG emission from 2020
  For +28% revenue
  Efficiency has improved
  Sustainability has not
Chart: Semiconductor market revenue
| 2020 | 2021
 | 475.41 | 608.03
Chart: Semiconductor vendors scope 1 + 2 total
| 2020 | 2021
Scope 1 | 31273419.6937 | 34436570.482
Scope 2 location-based | 49367321.3627 | 54123398.1878

## Slide 59: Semiconductor GHG accounting Limitations
Mixing location-based and market-based scope 2
  Underestimating scope 2
  When both numbers are available, market-based is lower by 7 to 75% (for Intel)
Extrapolating to others
  36% of revenues for semiconductor vendord
  8% of revenues for foundries
Missing scope 3
  Upstream: mining
  Downstream: usage and end-of-life
Budget granularity is company per company
  Retrieved from company estimations

## Slide 60: Where is semiconductor industry in global GHG emissions?
Global ICT impact is estimated up to 4%*
  55% from cloud and network infrastructure:
  45% from manufacturing devices
88 Mt CO2eq
0,15% of total
* Climat : l'insoutenable usage de la vidéo en ligne, the Shift Project, 2019

## Slide 61: Where are the %s total GHG of ICT?
Mines, smelters and refiners
Cloud computing facilities (scope 3 downstream)
  Including buildings, wiring…
Electronics cooling systems
Backbone fiber optics
  Including fiber optic connection work
Photonics and underwater cables
Screens – 30Mt CO2e in 2021
Batteries
…
CC-SA Project Kei

## Slide 62: Some data on semiconductor scope 3
Intel evaluates Scope 3 downstream
  22,9 Mt CO2eq in 2021 for product energy usage
    Use of yearly-produced electronics over lifetime
  Average product lifetime is estimated 4 years and 4 months
Intel evaluates Scope 3 upstream
  4,9 Mt CO2eq in 2021 for supply chain
  Does it include full mining impact or only part of the supply chain?

## Slide 63: How to Act on Electronics Sustainability?

## Slide 64: Actions towards Electronics Sustainability
Sustainable Development
Sustainable Electronics
Green Computing
Green Networking
Green IT
Sustainable ICT

## Slide 65: Where can electronics and computer science engineers act?
Collect and report the environmental footprint of electronics design decisions
Build products:
  With low energy consumption
  Repairable and modular
  Long-term upgradeable, with delayed obsolescence
  With ethical sourcing
  Favoring low carbon footprint and low waste suppliers
  Favoring low carbon footprint and low waste technologies
    ICs, batteries, PCBs, connectors, components, solar cells, supercapacitors…

## Slide 66: Open source hardware for sustainability
Fighting against obsolescence
  Long-term maintainance
    Linux is from 1991 !
  Superiority of community-based tools
    Examples of compilers: GCC, LLCM/Clang, etc.
  Stable APIs and interfaces
OSH tools for repair and reuse

## Slide 67: Actions towards Electronics Sustainability
European Green Deal on climate change – 2019
National laws: many in France
  Duty of vigilance 2017
  AGEC: lutte contre le gaspillage et à l'économie circulaire 2020
  REEN: réduire l'empreinte environnementale du numérique 2021
Labels and incentives
Projects: focus on open source hardware and ESOS

## Slide 68: How can Open Source Hardware help?

## Slide 69: What is open source hardware?
Open Source Hardware (definition by oshwa.org)
  hardware whose design is made publicly available so that anyone can study, modify, distribute, make, and sell the design, or hardware based on that design.
    In the form of mechanical drawings, schematics, bills of material, PCB layout data, HDL source code, and/or integrated circuit layout data
  The hardware's source, the design from which it is made, is available in the preferred format for making modifications to it. Ideally, open source hardware uses readily-available components and materials, standard processes, open infrastructure, unrestricted content, and open-source design tools to maximize the ability of individuals to make and use hardware.

## Slide 70: Types of open source hardware?
Open source hardware applies at three levels
  Printed circuit boards design – RPi, Arduino …
  Reconfigurable hardware design (FPGA)
  Integrated circuits design (ASIC)
Open source hardware applies in three forms
  Open source design tools
  Open source IPs (for Intellectual Property Block)
    To be integrated in own system
  Open source systems
    To be duplicated, repaired, transformed, enhanced, combined with

## Slide 71: A few open source hardware projects
Front-end design-level OSH
  gem5, GPGPUSim, McPAT, GPUWattch, SystemC simulation SoC simulators
  Verilator, Ghdl RTL simulators
  Gaut, LegUp, XLS, ScaleHLS High-Level Synthesis
Back-end design-level OSH
  ASIC
    Open-road and Alliance VLSI/CAD System
  FPGA
    IceStudio and open source FPGAs, openFPGA
Fabrication-level OSH
  Google Skywater PDK 130nm process

## Slide 72: Technological opportunities for sustainability
Slow performance improvement of single cores
Open hardware boom in digital ICs
  Large investments in RISC-V
  AI open-source developments reaching hardware

## Slide 73: The ESOS Project

## Slide 74: Part 2: ESOS
Electronics: Sustainable, Open, Sovereign
  Compétences et Métiers d'avenir - France2030, 2023-28
Notes: PIA: depuis 2010, dispositifs interministériels

## Slide 75: The ESOS project
Consortium led by INSA Rennes
  Consortium including INSA Rennes, University of Rennes, ENS Rennes, UIMM Bretagne, Novatech Industries (electronics courses covering a wide range of electronic design professions)
  Consortium teaching electronics in Bac+3/5/8, strong links with research
  30+ industrial partners
  6.38M€ of aid obtained, over 5 year
  Long-term objective of self-funding
  https://esos.insa-rennes.fr

## Slide 76: ESOS: Sustainable, Open, and Sovereign Electronics
Sustainable: that meets the needs of current generations without compromising the ability of future generations to meet their own needs.
Open: a decentralized development model that distributes source code publicly for open collaboration and peer production, called "the open source method.
Sovereign: the quality of the state being obliged or determined only by its own will, within the limits of the higher principle of law, and in accordance with the collective purpose it is called upon to achieve.

## Slide 77: ESOS Objectives
Objective 1: attract more students to the electronics field
  Raise awareness of the importance of electronics in environmental issues and increase the number of women in the industry
  Inform high school students about the challenges and opportunities of sustainable electronics
Objective 2: train teachers in sustainable electronics
  High school and university teachers
Objective 3: Train students in sustainable electronics
  Train future electronics engineers in product life cycle and eco-design
  Initial training and work-study programs in Bac+3, Bac+5, and Bac+8
Objective 4: train professionals in sustainable electronics
  Train current electronics engineers in the various aspects of sustainable development; in-service and online training

## Slide 78: Some ESOS courses to be developed
Life cycle analysis
  Eco-design
  Attributional and consequential GHG accounting
Open source HW
  For PCB design, for architecture design
  Contributing to large-scale open source projects
Electronics for the transitions
  Power electronics: novel substrates and technologies
Sustainability and open source versus:
  Cost, pure performance, safety, cybersecurity, …
Notes: The most important GHG accounting concept you
may not have heard of: the attributional-
consequential distinction

## Slide 79: Some ESOS courses to be developed
Sustainable business plans
  Open source valorisation
Legal aspects of sustainable electronics
  Lengthened guarantees
  Reparation-permitting guarantees
  Modification-permitting guarantees
  Systems parts storage
Notes: The most important GHG accounting concept you
may not have heard of: the attributional-
consequential distinction

## Slide 80: Questions?